## Slide 1
Wuqiong Luo
Chapter 8 Plane Electromagnetic Waves

## Slide 2
Contents
8.1 Plane Waves in Lossless Media
8.2 Plane Waves in Lossy Media
8.3 Flow of Electromagnetic Power and the
Poynting Vector
8.4 Normal Incidence at a Plane
Conducting Boundary
8.5 Normal Incidence at a Plane
Dielectric Boundary

## Slide 3
3
Basic Issues
Time-harmonic field
EM wave propagation
Infinite single media space
In passive region
Related concepts
1）Amplitude
2）phase
  time phase
  space phase
  Argument
  Initial Phase
3）Equal-phase Surface
4）Equal-Amplitude
Surface
Related concepts
Complex vector contains the changes
of field quantities at any time in space
8.1 Plane Waves in Lossless Media

## Slide 4
4
Problems
√ Plane Wave Cylindrical wave
Spherical wave
(The complex vector functions of fixed time)
Analysis of Time-harmonic EM Wave
Linear polarized wave
Circular polarized wave Elliptical polarized wave
(A fixed position of the instantaneous changes)
The law of the field quantities change with spatial location
The law of the field
quantities change with time
√
√
√

## Slide 5
5
The definition of uniform plane wave
Plane wave：At any time Equiphase Surface (wavefronts) is a flat sheet (plane)
Uniform plane wave
Uniform：The amplitude of the EM field in the equiphase surface is fixed
The equiphase surface of EM wave is plane, and also the
amplitude of EM field on the equiphase surface is a constant.
Features
Equi-phase surface and Equal-Amplitude Surface of uniform plane wave are coincidence or parallel
The electric field complex vector in equiphase surface(Eqs) is a constant vector
The amplitude and direction of the EM field in equi-phase surface are fixed at any time
Q：At different moments , the EM field in equi-phase surface of uniform plane wave is the same ？

## Slide 6
6
The ideal dielectric
Conductive medium

## Slide 7
7
1. The Electromagnetic Field of Uniform Plane Wave
Skills: establishing a proper coordinate system ！
take equiphase surface as coordinate plane ,such as x-y plane , thus：
Solution:
The instantaneous expression of the electric field
The EM wave propagate along the
direction of the spatial phase lag
then：

## Slide 8
8
Uniform plane wave is transverse
electromagnetic waves（TEM）
E
H
z
Wave propagation direction
Uniform plane wave
Wavefront
x
y
o
Important features

## Slide 9
9
The complex electromagnetic field vector of uniform plane wave that propagating along the z direction can express as ：
Uniform plane wave is transverse electromagnetic waves（TEM wave）
The EM wave propagate along the direction of the spatial phase lagging.
Summary

## Slide 10
10
Solution for uniform plane wave propagating along arbitrary direction
y
z
x
o
uniform plane wave propa-
gatiing along +Z direction
P(x,y,z)
r
Equiphase surface
So that:
To assume wave propagation direction:
uniform plane wave propa-
gatiing along arbitrary direction
direction of wave propagation
z
y
x
o
r
n
e
Equiphase surface
P(x,y,z)
Z’
For the convenience of said to define new physical quantities, Wave vector:
so
as the same
direction of wave propagation

## Slide 11
11
The composition of solution that corresponding UP-wave EM field
For the uniform plane wave propagate along , the expression
for electromagnetic field solutions：
The complex EM field vector：
where wave vector：
Transient solution of E：
The complex amplitude vector
The relationship
between and ?

## Slide 12
12
The technique of analyzing uniform plane wave and the EM field
expression using complex amplitude
Since:
Solution for EM field expressed using complex amplitude , when uniform plane wave propagating along
So:

## Slide 13
13
perpendicular to each other
Electric and magnetic fields in phase
Amplitude difference of times
The relationship between E and H of uniform plane wave
where
is the intrinsic impedance of the
medium, also called wave impedance
in vacuum
x
y
z
E
H
O
Uniform plane wave in ideal medium

## Slide 14
14
Solution for electromagnetic field complex vector ：
The direction of meet the Right-handed Corkscrew Rule
Transverse electromagnetic wave（TEM wave）
The direction of propagation along the space phase lag
Electric and magnetic fields in phase, amplitude difference of times
Summary for Uniform Plane Wave

## Slide 15
15
1、Propagation parameters of uniform plane wave
Period T ：At the same location, the time interval corresponding
phase change 2π
（1）Angular frequency, Frequency and Period
Angular frequency ω ： refers to the change of the phase per unit time, unit: rad /s
Frequency f ：
t
T
o
x
E

## Slide 16
16
（2）Wave length and Phase constant
Wave length λ ：At the same location, the space interval
corresponding phase change 2πof equiphase surface
Phase constant k： refers to the
change of the phase per unit
distance.（wave number）
o
x
E
l
z

## Slide 17
17
（3）Phase velocity
In vacuum ：
As
Phase velocity v：The velocity of equiphase surface moved in space.
Get the phase velocity of uniform plane wave is
independent with the
frequency of EM waves

## Slide 18
18
Solution for electromagnetic field complex vector：
The direction of meet the Right-handed Rule;
Transverse electromagnetic wave （TEM wave）
The direction of propagation along the space phase lagging
E and H in phase, amplitude difference of times;
Related physical quantities : frequency、period、wave length、phase constant 、wave number、phase velocity、power velocity
Summary for Uniform Plane Wave in Ideal Medium

## Slide 19: 8.1.2 polarization of electromagnetic wave
19
1. The concept of the polarization
2. Linear polarized wave
3. Circular polarized wave
4. Elliptical polarized wave
5. Polarized wave decomposition
6. Application of Polarization

## Slide 20
20
1：for harmonic field，due to the independent variable of the temporal variation can be separated，i.e. The law of the change of time and space are independent of each other. So ,when studying the law of time variation, the value of ，can take any value, such as :
The basic problem ：
For time varying electric field ,
at the fixed point ,to study the law of
Electric field change with time, such as
2： changing over time behave as its magnitude and direction is changing over time
Key points
conclusion：
Studying the law of time variation of harmonic field can be in any spatial location.
The study is focus on the change of the trajectory of the vector of the field over time.

## Slide 21
21
1. The concept of the polarization
At fixed point in the space, the trajectory of the E-field vector varies with time
The polarization of wave
Vector variation ，behave as the magnitude variation of the vector components;
Study of vector component changes over time，starting from the transient expression of field vector. for plane wave:
Analysis method
conclusion:
The rule of vector end changes over time is depend on the amplitude and initial phase of each component.
Any polarization can be synthesized by linear polarization！

## Slide 22
22
Without loss of generality，consider plane waves that propagate in the +z direction ，the expression is ：
The vector end equation
In rectangular
coordinate system：
（一） The vector end parametric equations
generally, nonlinear polarization
In polar coordinates：
（二） The vector end equation

## Slide 23
23
The mode of the polarization
Linear polarization
left-hand polarization (+Z)
conclusion: the mode of polarization for EM waves depends on the difference between initial phases of each component
right-hand polarization (-Z)
left-hand polarization (-Z)
right-hand polarization (+Z)

## Slide 24
24
2. linear polarized wave
time-varying
conclusion：Any two Linear polarized waves with the same frequency and direction of propagation, if their polarization direction perpendicular to each other, can be synthesized to a linear polarized wave, when their phase difference is zero or ±π.
constant
condition： or
then the vector parameter equation was simplified：

## Slide 25
25
3. Circular polarized wave
condition ：
constant
conclusion：Any two Linear polarized wave that the same frequency and direction of propagation, what’s more their polarization direction perpendicular to each other, can be synthesise to circular polarized wave, when their amplitude is the same and their differ phase is ±π/ 2 .
The vector end equation
Left-hand circular polarization wave(LHCP)
Right-hand circular polarization wave(RHCP)

## Slide 26
26
right-hand circular polarization wave
o
Ex
y
x
E
Ey
a
left-hand circular polarization wave：
right-hand circular polarization wave：
o
x
E
y
x
E
y
E
a
left-hand circular polarization wave

## Slide 27
27
Generally
4. elliptical polarized wave

## Slide 28
28
Summary of composite polarized wave
linear polarization：φ＝0、±
φ＝0，In quadrant 1, 3；φ＝± ，In quadrant 2,4
elliptical polarization：generally
for the wave in the +z direction : 0 < φ <  ，left-hand；－ < φ＜0，right-hand.
circular polarization：φ＝± /2，Exm＝Eym
for the wave in the +z direction :“＋” correspond to LHCP；“－” correspond to RHCP.
The polarized mode of electromagnetic wave is depend on the phase difference(φ＝φy－φx) and the amplitudes （Exm、Eym) of Exand Ey .
modes of polarization

## Slide 29
29
Ex. Illustrate the following uniform plane wave polarization mode.
( 1 )
( 2 )
( 3 )
Answer：
（1）
（2）
（3）
RHCP
linear polarized wave
RH elliptical polarized wave

## Slide 30
30
5. Polarized wave decomposition
Any kind of polarization of uniform plane wave can be decomposed into the sum of right- and left-hand circularly polarized wave, and their amplitude is different.
Any kind of polarization of uniform plane wave can be decomposed into the sum of two linear polarized wave .
Prove：
Any linear polarized wave can be decomposed into the sum of right- and left-hand circularly polarized wave, with equal amplitude.

## Slide 31
31
· Problems ！
· Analysis Method !
· The associated general
parameters and concepts!
· Typical problem in
application ？

## Slide 32
32
The polarization is wide used in many fields. such：
6. The engineering application of polarized wave
In radar target detection technology，Using the characteristics of the polarization changed in the process of electromagnetic scattering to achieve target recognition.
In the radio technology，Using the polarized characteristic of the antenna transmitting and receiving electromagnetic waves, to implement the best performance of radio signals transmitting and receiving.
In optical engineering , the different propagation characteristics of different polarized wave in the same material is used to design optical polarizing film, and so on .

## Slide 34
34
Solution for the electromagnetic field complex vector ：
the direction of perpendicular to each other, and meet the Right-handed Rule
The amplitude of E is times of the amplitude of H.
using the electric field vector trajectory to judge the polarization characteristics(using the relationship between the two vertical component of the electric field)
Related concepts and physical quantities：
frequency、period、wavelength、phase constant、wave number、phase velocity、power velocity、dispersion、the phenomenon of skin、skin depth、surface impedance、attenuation constant 、 phase constant、propagation constant、polarization (linear, circular, elliptic polarization; left-handed and
right-handed polarization）
Key points of the problem solving method
  basis on the direction of propagation , write the expression of electromagnetic field
  Solving physical quantities, Accord to the definition and the law.
The summary of single medium uniform plane wave

## Slide 35
35
The ideal dielectric
Conductive medium
8.2 Plane Waves in Lossy Media

## Slide 36
36
Given by，
then uniform plane wave along the z direction is：
1. Uniform Plane Wave in Conductive Medium
is propagation constant of EMW ，unit：1/m
is attenuation factor， is attenuation constant，unit：Np/m (nepers per meter)
is phase factor ， is phase constant，unit：rad/m（radian per meter）
The instantaneous electric field as
Amplitude attenuate in the form of index , is evanescent wave

## Slide 37
37
intrinsic impedance
E and H in Conductive Medium
E and H in Ideal dielectric
The corresponding magnetic field
intrinsic impedance is complex
The phase of Magnetic field is different with electric field , and lag its.

## Slide 38
38
Phase velocity is not only related with the medium parameters, but also related to the frequency of EM waves
propagation parameters

## Slide 39
39
Low Conductive Medium
2. Uniform Plane Wave in Low loss dielectrics (Special case)
The propagation characteristics of uniform plane wave in low conductive medium
The phase constant of low loss dielectrics is approximation to the phase constant of ideal medium

## Slide 40
40
Good Conductor：
3. Uniform Plane Wave in Good Conductor (Special case)
parameters of good conductive medium
wavelength：
phase velocity：

## Slide 41
41
skin effect：Since the attenuation constant is larger over higher frequency, and The high frequency EM wave can only exist in the surface layer of good conductor , it’s called the skin effect.
skin depth（ )：
intrinsic impedance
Corresponding the EM wave in good conductor, the phase of magnetic field is lagging with an angle of 45°compared with electric field
skin depth 
surface impedance （square resistivity ） ：
In the conductive medium , is the surface impedance always equal to the intrinsic resistance ?

## Slide 42
42
Cu：

## Slide 43
43
Table 1 Skin depth and surface resistance of some metal materials
Material Name | Conductivity σ /(S/m) | Skin Depthδ /m | Surface ResistivityRS /Ω
Silver | 6.17×107 |  | 
Red copper | 5.8×107 |  | 
Aluminum | 3.72×107 |  | 
Sodium | 2.1×107 |  | 
Brass | 1.6×107 |  | 
Stannum | 0.87×107 |  | 
Graphite | 0.01×107 |  | 

## Slide 44
44
Solution for electromagnetic field complex vector ：
The phases of Electric field and magnetic field are different. In addition, electric field phase advance magnetic field phase in an angle of , and its amplitude is times of magnetic field’s .
Related physical quantities :
dispersion, skin effect, the skin depth, surface impedance，attenuation constant，phase constant, propagation constant, and result in low conductive medium and good conductors
Summary for Plane Wave in Lossy Media

## Slide 45
45
Ex. 9.4 GHz uniform plane wave propagation in polyethylene (assuming that it’s lossless medium , εr = 2.26 ). The amplitude of magnetic field is 7mA/m , please get the phase velocity，wavelength , wave impedance and the amplitude of electric field.
Solution：from the question
So:

## Slide 46
46
Solution：Based on cosine, write directly
Ex. The amplitude of magnetic of uniform plane wave is 1/3π A/m , phase constant is
30 rad/m, spread in the air along the direction . If the direction of is , please write out the expression of , ,and the frequency and wavelength.
As β=30 rad/m，so
so:

## Slide 47
47
Ex. 100MHz uniform EM wave propagation in lossless medium (εr = 4, μr =1 ) along +Z . Electric field is .when t = 0 and z =1/8 m, the amplitude of the electric field is 10－4 V/m . Find the instantaneous value of electric and magnetic field.
Answer :Set the expression of the transient electric field intensity is
when t = 0、z =1/8 m ，the amplitude of the electric field is max ，
where

## Slide 48
48
So
The instantaneous value of the transient magnetic field is:
Where
So

## Slide 49
49
The energy flowing into volume V= Increased energy in the volume V + Energy loss in the volume V
1. Conservation of energy
Question： How to use mathematical representation ？
8.3 Flow of Electromagnetic Power and the Poynting Vector

## Slide 50
50
The energy density of electric field ：
The energy density of magnetic field ：
The total energy density of electromagnetic field ：
The total energy of electromagnetic field
in the volume V ：
Features：When the electromagnetic field changes with time, the electromagnetic field energy density at each point of the space also changes with time, which causes the flow of electromagnetic energy.
Storage of Electromagnetic energy in the volume V
Conclusion: describe the relationship of
energy according to the storage energy
changed with time.

## Slide 51
51
Subtract the above two equations:
According to
The mathematical representation for the conservation of energy ──Poynting theorem

## Slide 52
52
Integral form (relationship for instantaneous power) ：
The Poynting theorem and its physical meaning
Differential form (relationship for instantaneous power density) ：
Electromagnetic power increased in the volume V
Power loss in the volume V
the power is flowing into volume V
（ New physical quantity ）

## Slide 53
53
Definition： ( W/m2 )
Physical meaning ：
Direction of — The direction of electromagnetic energy transmission
Value of ——
It describes the characteristics of the electromagnetic energy transmission (flow) in the time varying electromagnetic field
The Poynting vector (energy flow density vector)
Flow of power per unit area
it is the electromagnetic power per unit area at the perpendicular the transmission direction of the energy

## Slide 54
54
2、Power density and Power flow density
where,
The electric field energy and the magnetic field energy of uniform plane wave in ideal medium is equal.
Power density :
Power flow density :
Relationship :
The energy velocity and the phase velocity of uniform plane wave in ideal medium is equal

## Slide 55
55
Instantaneous power relation ：
Instantaneous power density relation：
Instantaneous energy density and energy flow density vector
Notice：
all the variables in the formula must be represented by real form.
the real form of each variable need to be used when doing calculation.

## Slide 56
56
Ex： The calculation of the instantaneous Poynting vector
Ex： Calculation of the electric field energy density of instantaneous storage
Ex：Calculation of instantaneous power density consumption
When solving the problems ,the instantaneous expression of the field must be written ！

## Slide 57
57
Time average definition of time functions：
Average energy / power density and energy flow density vector
it is a periodic function with time T

## Slide 58
58
The average Poynting vector （ energy flow density vector）
When solving the problems ,the instantaneous expression of the source is not required to be written ！

## Slide 59
59
Average electric field energy density
When solving the problems ,the instantaneous expression of the source is not required to be written ！

## Slide 60
60
Average magnetic field energy density
When solving the problems ,the instantaneous expression of the source is not required to be written ！

## Slide 61
61
Average Joule loss power density
When solving the problems ,the instantaneous expression of the source is not required to be written ！

## Slide 62
62
Sloution：The complex expression of electric field is
The intrinsic impedance of free space is
Get the expression of magnetic field
So , the average Poynting vector is
The average power of vertical cross a round plane is
Ex. The electric field intensityof plane wave in free space
find the average power of vertical cross a round plane (radius=2.5m) at z = z0.

## Slide 63
63
Solution：（1）Due to ， So
So
Ex. The complex expression magnetic field intensity of plane wave in air is
Where A is constant . Get the :1) ；2）wavelength and frequency；3）the value of A；4）The complex expression electric field；5）average Poynting vector .

## Slide 64
64
（2）
（3）
（4）
（5）

## Slide 65
65
Ex. Polarized （in the X direction ）waves propagating in sea along + z . The parameter of the sea is εr = 81 、 μr =1 、σ= 4 S/m , At z = 0, Ex = 100cos(107πt ) V/m .Please work out ：
（1）The attenuation constant, phase constant, intrinsic impedance, phase velocity, wavelength and skin depth ；
（2）The distance of wave propagation, when he amplitude of the electric field intensity reduced to be 1/1000 of the value at z=0.
（3）The expression of instantaneous electric and magnetic field intensity at z = 0.8 m ；
（4）Average power per 1m2 at z=0.8m 。
Sloution：（1）According to the problem
So
In this condition, the sea can be regarded as good conductor.

## Slide 66
66
So , Attenuation constant
Phase constant
The characteristic
impedance
Phase velocity
Wavelebgth
Skin depth

## Slide 67
67
（2） Let e-αz＝1/1000， i.e. eαz＝1000，can get the distance of wave propagation, when the amplitude of the electric field intensity reduced to be 1/1000 of the value at z=0
So at z = 0.8 m, the expression of instantaneous electric field is
the expression of instantaneous magnetic field is
（3）According to the problem, the expression of instantaneous electric field intensity is

## Slide 68
68
（4）At z = 0.8 m ,the average Poynting vector
The average power acoss The average
power acoss 1m2 is Pav = 0.75 mW
It can be known that the EM wave attenuation is very fast, especially at high frequency, the attenuation is more serious. This has led to a lot of difficulties for the communication between the submarines. To have lower attenuation, the working frequency must be very low, but even at the low frequency of 1 kHz, the attenuation is still obvious.
The curve of the skin depth of the sea changes with the frequency

## Slide 69
69
Ex. In the electromagnetic measurement, in order to prevent the indoor electronic equipment from the outside world the influence of electromagnetic field，Copper plate can be used to construct shielding room, usually require copper thickness greater than 5δ . If the require frequency range is from 10KHz to 100MHZ , Calculate how thick copper plate at least。the parameter of Cu :μ=μ0、ε=ε0、σ = 5.8×107 S/m。
Answer ：For the frequency range of low-end fL =10kHz ，
For the frequency range of high-end fH =100MHz ，

## Slide 70
70
this shows , copper can be treat as good conductor in the required frequency range of ，
In order to satisfy a given frequency range of the shielding requirements，
The thickness of the copper plate at least should be

## Slide 71
71
Phenomenon：
In the space , at the side of the incident wave of electromagnetic wave added a reflected wave ; the transmitted wave can exist on the other side .
The incident way：
vertical incidence 、
oblique incidence
Medium：
Conductive medium, ideal conductor, the ideal dielectric
i
q
r
q
t
q
z
x
y
i
E
//
i
E
i
^
E
incident wave
reflected wave
transmitted wave
interface
Plane of incidence
//
r
E
r
^
E
r
E
t
^
E
t
E
//
t
E
i
k
r
k
t
k
8.4 Normal Incidence at a Plane Conducting Boundary

## Slide 72
72
The basic problem：
To solve the incident wave and transmission wave electromagnetic fields respectively
Incident wave space：
Transmission wave space：
problem：
Known:
Solve:
Find the direction and the value of the corresponding physical quantities.
i
q
r
q
t
q
z
x
y
i
E
//
i
E
i
^
E
incident wave
reflected wave
transmitted wave
interface
Plane of incidence
//
r
E
r
^
E
r
E
t
^
E
t
E
//
t
E
i
k
r
k
t
k

## Slide 73
73
boundary condition
incident wave（known）
＋reflected wave（unknown）
Analysis Method ：
Establish the relationship of various physical quantities on the boundary
i
q
r
q
t
q
z
x
y
i
E
//
i
E
i
^
E
incident wave
reflected wave
transmitted wave
interface
Plane of incidence
//
r
E
r
^
E
r
E
t
^
E
t
E
//
t
E
i
k
r
k
t
k
transmitted wave (unknown)

## Slide 74
74
Uniform plane wave vertical incidence to the interface between two different media plane
feature：
The reflection wave propagation along the -z direction. the transmitted wave propagation along the +z direction
the electric field only has x component
why？
(Determine the direction of physical quantities of reflected and transmission wave !)

## Slide 75
75
z
x
medium1：
medium2：
y
Assuming that the incident wave is linear polarized wave at x direction
at z < 0 region，the parameters of conductive medium1
at z > 0 region，the parameters of conductive medium 2
Establish coordinate system as shown
without loss of generality ！why？
How is for circular polarized wave？
problem：solve the amplitude of reflected wave and transmission wave
method：write out the expression and use the boundary conditions

## Slide 76
76
incident wave in medium 1：
reflected wave in medium 1 ：
transmitted wave in medium 2：

## Slide 77
77
where：
Reflection coefficient on the interface
Transmission coefficient on the interface

## Slide 78
78
x
medium1：
medium 2：
z
z = 0
y
medium 1 is ideal dielectric，σ1＝0
medium 2 is ideal conductor，σ2＝∞
so
incident wave in medium 1：
reflected wave in medium 1：
then
on the interface，the Phase difference between the incident wave and reflected wave is π

## Slide 79
79
the electromagnetic field of total field in miduim 1
Instantaneous value form
electric field intensity
magnetic field intensity
incident wave
total wave
reflected wave
the relationship of the total fields：
time phase difference isπ/2
space length difference is λ/4

## Slide 80
80
the average poynting vector of the total field is :
the induced current density on the surface of the ideal conductor
The relevant physical quantities and concepts
travelling wave：Electromagnetic wave propagated along a certain direction in the space (moving)
Standing wave： Electromagnetic wave is not propagated in the space，there are antinodes and nodes at fixed point.
travelling-standing wave ：part of the electromagnetic wave in space spread, and part of don't spread.

## Slide 81
81
travelling wave along z
standing wave
electric field intensity
magnetic field intensity
incident wave
total
wave
reflected wave
travelling wave along -z
the point of antinodes ( the point of the maximum value of electric field)：
The distance from conducting plate is
(n = 0,1,2,3,…)
the point of nodes（the point of the minimum value of electric field）：
(n = 0,1,2,3,…)
The distance from conducting plate is

## Slide 82
82
where：
Reflectance coefficient on the interface
Transmission coefficient on the interface
The electromagnetic field in the both sides of general medium interface

## Slide 83
83
Assume that two kinds of medium are the ideal dielectrics，1= 2= 0
so
Discuss
when η2 >η1，Γ > 0，the electric field of reflected wave and incidence wave is the same in phase.
when η2 <η1，Γ < 0， the electric field of reflected wave and incidence wave is reverse in phase.
x
dielectrics 1：
dielectrics 2：
z
z=0
y
8.5 Normal Incidence at a Plane Dielectric Boundary

## Slide 84
84
incidence wave
reflected wave
transmitted wave
total：
— the electric field of total field
— the electric field of standing wave
z
— the electric field of travelling wave
travelling-standing wave
x
x

## Slide 85
85
The amplitude change of the total electric field in the ideal dielectric
optically denser medium（ < 0）
——the amplitude of the total electric field
—— the electric field of total field
z
z =－nλ1/ 2
z =－(n/2+1/4)λ1
x

## Slide 86
86
The change rule in the space for the amplitude of the total electric field in the ideal dielectric
Light thin medium（ > 0）
z =－nλ1/ 2
z =－(n/2+1/4)λ1
z
x
——the amplitude of the total electric field
—— the electric field of total field

## Slide 87
87
Question and Thinking：
  1） Whether the amplitude of travelling wave in the ideal dielectric will by change with different space position?
  2）What is the standing wave?
  3）Reflected wave is travelling wave or standing wave?
  4）what wave is the total field wave？
  5）Why the amplitude of total field will by changed with different space position?
  6）What is the reason for standing wave？
  reflection standing wave

## Slide 88
88
standing-wave ratio (SWR) S
Discuss
when Г＝0 , S ＝1, travelling wave.
when Г＝±1 , S =  , Pure standing-wave.
when , 1< S < ，Mixed wave. With the value of S increase, the component of standing wave increase ,and the component of the travellling wave reduce.
Introducing a new quantity to express standing wave or the degree of reflection

## Slide 89
89
The average power density in the dielectric 2
The average power density propagate along Z in the dielectric 1
Electromagnetic energy flow density
due

## Slide 90
90
Ex. uniform plane wave propagate along +Z, the electric field intensity vector is
Solution: (1) The expressions of the complex of the electric field intensity
Find:
（1）the corresponding magnetic field intensity ;
（2）if on the direction of propagation at the point of z = 0，place an infinite plate of ideal conductor, write out the electric and magnetic field intensity in the z < 0 region ;
（3）the electric current density on the surface of ideal conductor.
so

## Slide 91
91
the instantaneous expression:
(2) the electric field of the reflected wave is
the magnetic field of the reflected wave is

## Slide 92
92
the expressions of electric and magnetic field of the total field in the z < 0 region, respectively
(3) the electric current density on the surface of ideal conductor is

## Slide 93
93
Ex. In the free space, uniform plane wave vertical incidence to the semi infinite plane of lossless dielectric. Given the SWR=3 in the free space, the wavelength in the dielectric is 1/6 of that in the space. The point of the minimum value of standing wave is on the interface. Work out the relative permeability and relative permittivity of the dielectric.
Answer ：Due to SWR is
as the point of the minimum value of standing wave is on the interface
because the wavelength
in 2 region
as reflection coefficient
where

## Slide 94
94
Ex. The electric field of incidence wave is .
it vertical incident to the interface at z = 0 from the region (z < 0) of air (μr=1 εr = 4) . Find the electric and magnetic fields in the region of z > 0.
Solution: the intrinsic impedance in the z > 0 region
Transmission coefficient
medium 1
medium 2
z
x
y

## Slide 95
95
phase constant
so

## Slide 96
96
Ex. Given the parameters of medium 1 are εr1=4、μr1=1、σ1=0 ； medium 2 : εr2=10、μr2 = 4、σ2= 0 . A uniform plane wave which its angular frequency is ω＝5×108 rad /s vertical incidence to the interface from medium 1 . The incidence wave is linear polarized wave in the direction of x axis , when t＝0、z＝0 ，the amplitude of incidence wave is 2.4 V/m . Find:
(1) β1 and β2 ；
(2) reflection coefficient Г1 andГ2 ；
(3) the electric field in the region 1 ；
(4) the electric field in the region 2 .
Solution:（1）

## Slide 97
97
（2）
（3） the electric field in the region 1

## Slide 98
98
（4）
so
or

## Slide 99
99
In the space of incidence wave there are incidence wave and reflected wave , only transmitted wave in the transmitted space
The direction of incidence、reflected and transmitted wave both in the normal direction of the interface.
The direction of electromagnetic field of incidence、reflected and transmitted wave both in the same coordinate axis direction.
Incidence, reflection and transmission wave respectively satisfy the propagation rules in a single dielectric space.
Related concepts and physical quantities：
Travelling wave 、standing wave 、travelling-standing wave, reflection coefficient 、 transmission coefficient, standing wave coefficient (SWR), antinodes, node, light dense medium, light thinner medium
Key points for the problem solving method:
  Basis on the incidence wave, written expressions of reflected wave and transmitted wave respectively. Then analysis and discuss the related total wave.
  According to the definition and the law to work out the physical quantities.
Summary

## Slide 100: Homework
8-5, 8-6, 8-12, 8-17, 8-22, 8-27