## Slide 1
Fundamentals of Analogue Circuits
Hongling Cui

## Slide 2
Fundamentals of Analogue Circuits
Chapter 4 Diodes
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 3
Fundamentals of Analogue Circuits
Introduction
IN THIS CHAPTER WE WILL LEARN
  1. the characteristics of the ideal diode and how to analyze and design circuits containing multiple ideal diodes together with resistors and dc sources to realize useful and interesting nonlinear function.
  2. the details of the i-v characteristic of the junction diode (which was derived in Chapter 3) and how to use it to analyze diode circuits operating in the various bias regions: forward, reverse, and breakdown.

## Slide 4
Fundamentals of Analogue Circuits
Introduction
  3. a simple but effective model of the diode i-v characteristic in the forward direction: the constant-voltage-drop model
4. a powerful technique for the application and modeling of the diode (and in later chapters, transistors): dc-biasing the diode and modeling its operation for small signals around the dc-operating point by means of the small-signal model

## Slide 5
Fundamentals of Analogue Circuits
5. the use of a string of forward-biased diodes and of diodes operating in the breakdown region (zener diodes), to provide constant dc voltages (voltage regulators)
6. application of the diode in the design of rectifier circuits, which convert ac voltages to dc as needed for powering electronic equipment

## Slide 6
Fundamentals of Analogue Circuits
4.1.1. Current-Voltage Characteristic of the Ideal Diode
ideal diode – most fundament nonlinear circuit element
  two terminal device
  circuit symbol shown to right
Figure 4.1: Diode characteristics
cathode – negative terminal, from which current flows
anode – positive terminal of diode, into which current flows

## Slide 7
Fundamentals of Analogue Circuits
ideal diode
  operates in two modes
    on and off
Figure 4.1: Diode characteristics
mode#1: reverse bias = open ckt

## Slide 8
Fundamentals of Analogue Circuits
ideal diode
  operates in two modes
    on and off
Figure 4.1: Diode characteristics
mode#2: forward bias = short ckt
mode#1: reverse bias = open ckt

## Slide 9
Fundamentals of Analogue Circuits
External circuit should be designed to limit…
Figure 4.2: The two modes of operation of ideal diodes and the use of an external circuit to limit (a) the forward current and (b) the reverse voltage.
  current flow across conducting diode
  voltage across blocking diode
Examples are shown to right…

## Slide 10
Fundamentals of Analogue Circuits
ideal diode
  operates in two modes
    on and off

## Slide 11
Fundamentals of Analogue Circuits
4.1.2 A Simple Application – The Rectifier
One fundamental application of this piecewise linear behavior is the rectifier.
Q: What is a rectifier?
  A: Circuit which converts AC waves in to DC…ideally with no loss.
Figure 4.3(a): Rectifier Circuit

## Slide 12
During the positive half-cycles of the input sinusoid, the diode turn on.
Fundamentals of Analogue Circuits

## Slide 13
During the negative half-cycles of the input sinusoid, the diode turn off.
Fundamentals of Analogue Circuits

## Slide 14
Fundamentals of Analogue Circuits
Example 4.1 Diode Rectifier
Figure 4.4: Circuit for Example 4.1.
Figure 4.4(a) shows a circuit for charging a 12-V battery. If vS is a sinusoid with 24-V peak amplitude, find the fraction of each cycle during which the diode conducts. Also, find the peak value of the diode current and the maximum reverse-bias voltage that appears across the diode.

## Slide 15
  Q(a): Find the fraction of each cycle during which the diode conducts.
  Q(b): Find peak value of diode current and maximum reverse-bias voltage that appears across the diode.
Fundamentals of Analogue Circuits
Figure 4.4: Circuit and Waveforms for Example 4.1.

## Slide 16
Fundamentals of Analogue Circuits
Thus θ =60°and the conduction angle is 120.
The peak value of the diode current is given by
The maximum reverse voltage is equal to 24+12=36V.

## Slide 17
Fundamentals of Analogue Circuits
ideal diode
  operates in two modes
    on and off
Figure 4.1: Diode characteristics
mode#2: forward bias = short ckt
mode#1: reverse bias = open ckt

## Slide 18
Fundamentals of Analogue Circuits
Example 4.2 (Assumed States Method)
Assuming the diodes to be ideal, find the values of I and V
Application of hypothesis method

## Slide 19
Fundamentals of Analogue Circuits
Example 4.2
Assuming the diodes to be ideal, find the values of I and V
Solution:
assume that both diodes are conducting
VB =0 and V =0
The current through D2 can be determined from
Writing a node equation at B
then

## Slide 20
Fundamentals of Analogue Circuits
Example 4.2
Assuming the diodes to be ideal, find the values of I and V
Solution:
assume that both diodes are conducting
VB =0 and V =0
The current through D2 can be determined from
Writing a node equation at B
then
Notes: .

## Slide 21
Fundamentals of Analogue Circuits
Example 4.2
Assuming the diodes to be ideal, find the values of I and V
Solution:
assume D1 is off and D2 is on
The current through D2 can be determined from
Then the voltage at node B is
Therefor D1 is reverse biased as assumed.

## Slide 22
Fundamentals of Analogue Circuits
4.2. Terminal Characteristics of Junction Diodes
Most common implementation of a diode utilizes pn junction.

## Slide 23
Fundamentals of Analogue Circuits
Example: measurement of i–v characteristic of 1N4001
Measurement data
measurement of circuit
mA
V
E
R
D
vD | iD
0.000V | 0.000μA
0.100V | 0.189μA
0.200V | 1.496μA
0.300V | 10.527μA
0.400V | 72.940μA
0.500V | 504.126μA
0.535V | 1.000mA
0.571V | 2.000mA
0.592V | 3.000mA
0.600V | 3.476mA
0.700V | 23.625mA
0.800V | 147.375mA
0.900V | 663.944mA
1.000V | 1.796A
4.2.1. The Forward-Bias Region

## Slide 24
Fundamentals of Analogue Circuits
Example: measurement of i–v characteristic of 1N4001
Measurement data
measurement of circuit
mA
V
E
R
D
vD | iD
0.000V | 0.000μA
0.100V | 0.189μA
0.200V | 1.496μA
0.300V | 10.527μA
0.400V | 72.940μA
0.500V | 504.126μA
0.535V | 1.000mA
0.571V | 2.000mA
0.592V | 3.000mA
0.600V | 3.476mA
0.700V | 23.625mA
0.800V | 147.375mA
0.900V | 663.944mA
1.000V | 1.796A

## Slide 25
Fundamentals of Analogue Circuits
Example: measurement of i–v characteristic of 1N4001
Measurement data
vD | iD
0.000V | 0.000μA
0.100V | 0.189μA
0.200V | 1.496μA
0.300V | 10.527μA
0.400V | 72.940μA
0.500V | 504.126μA
0.535V | 1.000mA
0.571V | 2.000mA
0.592V | 3.000mA
0.600V | 3.476mA
0.700V | 23.625mA
0.800V | 147.375mA
0.900V | 663.944mA
1.000V | 1.796A
The i–v characteristic of the forward…
fully conducting region

## Slide 26
Fundamentals of Analogue Circuits
4.2.1. The Forward-Bias Region
I-V relationship is closely approximated by equations to right.
The forward-bias region of operation is entered when v > 0.
where IS is a constant for a given diode at a given temperature.
the voltage VT is a constant called the thermal voltage.
At room temperature (20°C) the value of VT is 25.3 mV. In rapid approximate circuit analysis we shall use VT ≈25mV at room temperature.

## Slide 27
Fundamentals of Analogue Circuits
4.2.1. The Forward-Bias Region
The forward-bias region of operation is entered when v > 0.
I-V relationship is closely approximated by equations to right.
when

## Slide 28
Fundamentals of Analogue Circuits
Q: What is the relative effect of current flow (i) on forward biasing voltage (v)?
A: Very small.
  10x change in i, effects 60mV change in v.

## Slide 29
Fundamentals of Analogue Circuits
reverse-bias
μA
V
E
R
D
uD | iD
0.000V | 0.000μA
-0.0625V | -0.022μA
-0.125V | -0.029μA
-0.250V | -0.032μA
-0.500V | -0.032μA
-1.000V | -0.033μA
-2.000V | -0.034μA
-4.000V | -0.036μA
-8.000V | -0.040μA
-16.000V | -0.048μA
-32.000V | -0.064μA
-50.000V | -0.082μA
-52.907V | -1.000μA
-53.027V | -100.000μA
-53.147V | -10.000mA
Measurement data
4.2.2. The Reverse-Bias Region

## Slide 30
Fundamentals of Analogue Circuits
4.2.2. The Reverse-Bias Region
The reverse-bias region of operation is entered when v < 0.
I-V relationship, for negative voltages with |v| > 3VT (25mV), is closely approximated by equations to right.

## Slide 31
Fundamentals of Analogue Circuits
reverse-bias
μA
V
E
R
D
vD | iD
0.000V | 0.000μA
-0.0625V | -0.022μA
-0.125V | -0.029μA
-0.250V | -0.032μA
-0.500V | -0.032μA
-1.000V | -0.033μA
-2.000V | -0.034μA
-4.000V | -0.036μA
-8.000V | -0.040μA
-16.000V | -0.048μA
-32.000V | -0.064μA
-50.000V | -0.082μA
-52.907V | -1.000μA
-53.027V | -100.000μA
-53.147V | -10.000mA
Measurement data
4.2.3 The Breakdown Region

## Slide 32
Fundamentals of Analogue Circuits
vD | iD
0.000V | 0.000μA
-0.0625V | -0.022μA
-0.125V | -0.029μA
-0.250V | -0.032μA
-0.500V | -0.032μA
-1.000V | -0.033μA
-2.000V | -0.034μA
-4.000V | -0.036μA
-8.000V | -0.040μA
-16.000V | -0.048μA
-32.000V | -0.064μA
-50.000V | -0.082μA
-52.907V | -1.000μA
-53.027V | -100.000μA
-53.147V | -10.000mA
Measurement data
The i–v characteristic of the reverse…
4.2.2. The Reverse-Bias Region

## Slide 33
The breakdown region of operation is entered when v < VZK.
  Zener-Knee Voltage (VZK)
Fundamentals of Analogue Circuits
4.2.3 The Breakdown Region
breakdown region
This is normally
non-destructive.
Imax< Pmax/VZ

## Slide 34
Fundamentals of Analogue Circuits
Terminal Characteristics of Junction Diodes
I-V curve consists of three characteristic regions
  forward bias: v > 0
  reverse bias: v < 0
  breakdown: v <-VZK

## Slide 35
Fundamentals of Analogue Circuits
Since both IS and VT are functions of temperature, the forward i–v characteristic varies with temperature
Figure 4.9 Temperature dependence of the diode forward characteristic. At a constant current, the voltage drop decreases by approximately 2 mV for every 1°C increase in temperature.
Temperature Effects

## Slide 36
Fundamentals of Analogue Circuits
cut-in voltage – is voltage, below which, minimal current flows
  approximately 0.5V
fully conducting region
fully conducting region – is region in which Rdiode is approximately equal 0
  between 0.6 and 0.8V

## Slide 37
Fundamentals of Analogue Circuits
4.3. Modeling the Diode Forward Characteristic
Discuss simplified diode models better suited for use in circuit analyses:
  exponential model
  constant voltage-drop model
  ideal diode model
  small-signal (linearization) model

## Slide 38
Fundamentals of Analogue Circuits
4.3.1 The Exponential Model
exponential diode model
  most accurate
  most difficult to employ in circuit analysis
    due to nonlinear nature

## Slide 39
Fundamentals of Analogue Circuits
4.3.1 The Exponential Model
Q: How does one solve for ID in circuit to right?
  VDD = 5V
  R = 1kΩ
  ID = 1mA @ 0.7V
Figure 4.10: A simple circuit used to illustrate the analysis of circuits in which the diode is forward conducting.
A: Two methods exist…
  graphical method
  iterative method

## Slide 40
Fundamentals of Analogue Circuits
step1: Plot the relationships of these two equations on single graph
step 2: Find intersection of the two curves
  load line and diode characteristic intersect at operating point
Figure 4.11: Graphical analysis of the circuit in Fig. 4.10 using the exponential diode model.
4.3.2 Graphical Analysis Using the Exponential Model

## Slide 41
Fundamentals of Analogue Circuits
Pro’s
  Intuitive
Con’s
  Poor Precision
  Not Practical for Complex Analyses
Figure 4.11: Graphical analysis of the circuit in Fig. 4.10 using the exponential diode model.

## Slide 42
Fundamentals of Analogue Circuits
4.3.1 The Exponential Model
  VDD = 5V
  R = 1kΩ
  ID = 1mA @ 0.7V
Assume VD =0.7V
= 4.3mA

## Slide 43
Fundamentals of Analogue Circuits
4.3.1 The Exponential Model
  VDD = 5V
  R = 1kΩ
  ID = 1mA @ 0.7V
Assume VD =0.7V
= 4.3mA
Substituting 2.3VT =60mV, V1 =0.7V, I1 =1mA, and I2 =4.3mA results in V2 =0.738V.

## Slide 44
Fundamentals of Analogue Circuits
4.3.3 Iterative Analysis Using the Exponential Model
ID= 4.262 mA
V2 = 0.738 V
I2 =4.3mA
V2 =0.738V

## Slide 45
Fundamentals of Analogue Circuits
4.3.3 Iterative Analysis Using the Exponential Model
ID= 4.262 mA
V2 = 0.738 V

## Slide 46
Fundamentals of Analogue Circuits
4.3.5. The Constant Voltage-Drop Model
Q: How can one analyze these diode-based circuits more efficiently?
A: Find a simpler model.
  One example is assume that voltage drop across the diode is constant.

## Slide 47
Fundamentals of Analogue Circuits
The constant voltage-drop diode model assumes that the slope of ID vs. VD is vertical @ 0.7V
the model of the foward–conducting diodes
approximating the exponential characteristic by a constant voltage

## Slide 48
Fundamentals of Analogue Circuits
Q: How does example 4.4 solution change if CVDM is used?
  A: 4.262mA to 4.3mA
5V
1kΩ
5V
1kΩ

## Slide 49
Fundamentals of Analogue Circuits
The ideal diode model assumes that the slope of ID vs. VD is vertical @ 0V
Q: How does example 4.4 solution change if ideal model is used?
  A: 4.262mA to 5mA
5V
1kΩ

## Slide 50
Fundamentals of Analogue Circuits
How to use these models?
exponential model
  low voltages
  less complex circuits
  emphasis on accuracy over practicality
constant voltage-drop mode:
  medium voltages = 0.7V
  more complex circuits
  emphasis on practicality over accuracy
ideal diode model
  high voltages >> 0.7V
  very complex circuits
  cases where a difference in voltage by 0.7V is negligible

## Slide 51
Fundamentals of Analogue Circuits
R
D
VDQ
iD
vD
VD
4.3.7 Small-Signal Model
Why we need the small signal method?
  transmit the signal through nonlinear devices.
  No distortion.
t

## Slide 52
Fundamentals of Analogue Circuits
Q
O
vd
vD
t
Q’
Q”
VD
R
D
IDQ
VDQ
iD
vD
VD
VD/R
total signal
DC offset
Small signal

## Slide 53
Fundamentals of Analogue Circuits
Q
IDQ
VDQ
iD
vD
O
VD
VD/R
Δv
(VD+Δv)/R
Δvd
Δid
VD
R
D

## Slide 54
Fundamentals of Analogue Circuits
Q: How is the small-signal diode model defined?
  step #1: Consider the conceptual circuit of Figure 4.13(a).
    DC voltage (VD) is applied to diode
    Upon VD, arbitrary time-varying signal vd is super-imposed

## Slide 55
Fundamentals of Analogue Circuits
step #2: Define DC current as in (4.8).
step #3: Define total instantaneous voltage (vD) as composed of VD and vd.
step #4: Define total instantaneous current (iD) as function of vD.
VD
R
D
+
-

## Slide 56
Fundamentals of Analogue Circuits
step #5: replace vD with (VD+vd ).
step #6: Split this exponential in two.
step #7: Redefine total instant current in terms of DC component (ID) and time-varying voltage (vd).

## Slide 57
Fundamentals of Analogue Circuits
step #8: Apply power series expansion to (4.12).
step #9: Because vd/VT << 1, certain terms may be neglected.

## Slide 58
Fundamentals of Analogue Circuits
small signal approximation
  Shown to right for exponential diode model.
    total instant current (iD)
    small-signal current (id.)
    small-signal resistance (rd.)
  Valid for for vd < 5mV amplitude (not peak to peak).

## Slide 59
Fundamentals of Analogue Circuits
Q: How is small-signal resistance rd defined?
  A: From steady-state current (ID) and thermal voltage (VT) as below.
    Note this approximation is only valid for small-signal voltages vd < 5mV.
T=20℃：

## Slide 60
Fundamentals of Analogue Circuits
Quiescent point
Another solution is to seek derivatives.

## Slide 61
Fundamentals of Analogue Circuits
differentiate：
T=20℃：

## Slide 62
Fundamentals of Analogue Circuits
Q
O
vd
vD
t
Q’
Q”
VD
R
D
IDQ
VDQ
iD
vD
VD
VD/R

## Slide 63
Fundamentals of Analogue Circuits
Summary of Small-Signal Model
  The total instantaneous circuit is divided into steady-state and time varying components, which may be analyzed separately and solved via algebra.
    In steady-state, diode represented as CVDM.
    In time-varying, diode represented as resistor.

## Slide 64
Fundamentals of Analogue Circuits
A systematic procedure for finding incremental voltages and currents for a circuit containing a diode is as follows:
1. Find the DC operating variables, ID and VD, using the subcircuit derived from the original circuit by setting all small-signal sources to zero..

## Slide 65
Fundamentals of Analogue Circuits
A systematic procedure for finding incremental voltages and currents for a circuit containing a diode is as follows:
1. Find the DC operating variables, ID and VD, using the subcircuit derived from the original circuit by setting all small-signal sources to zero..
2. Find the small signal (incremental) voltage and the small signal diode current by forming a small signal subcircuit in which the diode is replaced by a resistor of value rd, and all DC sources are set to zero.

## Slide 66
Fundamentals of Analogue Circuits
Example 4.5 Small-Signal Model
The power supply V+ has a dc value of 10V over which is superimposed a 60Hz sinusoid of 1V peak amplitude (known as the ripple)
Assume diode to have 0.7V drop at 1mA current.
  Q: Calculate the amplitude of the sine-wave signal appearing across the diode.
10kΩ

## Slide 67
Fundamentals of Analogue Circuits
And small signal analysis comprises the following steps:
Find the DC operating variables ID and VD by setting all small-signal sources to zero.
Find the incremental device voltage vd by forming a small signal subcircuit in which the diode is replaced by a linear resistor of value rd, and all DC sources are set to zero.

## Slide 68
Fundamentals of Analogue Circuits
10kΩ
Considering dc quantities only, we assume VD ≈ 0.7 V and calculate the diode dc current
At this operating point, the diode incremental resistance rd is

## Slide 69
Fundamentals of Analogue Circuits
The signal voltage across the diode can be found from the small-signal equivalent circuit
Using the voltage-divider rule provides the peak amplitude of vd as follows:
10kΩ

## Slide 70
Fundamentals of Analogue Circuits
Example 4.5 Small-Signal Model
The power supply V+ has a dc value of 10V over which is superimposed a 60Hz sinusoid of 1V peak amplitude (known as the ripple)
Assume diode to have 0.7V drop at 1mA current.
  Q: Calculate the amplitude of the sine-wave signal appearing across the diode.
10kΩ

## Slide 71
Fundamentals of Analogue Circuits
10kΩ
Considering dc quantities only, we assume VD ≈ 0.7 V and calculate the diode dc current
At this operating point, the diode incremental resistance rd is

## Slide 72
Fundamentals of Analogue Circuits
The signal voltage across the diode can be found from the small-signal equivalent circuit
Using the voltage-divider rule provides the peak amplitude of vd as follows:
10kΩ

## Slide 73
Fundamentals of Analogue Circuits
4.3.8 Voltage Regulation
Q: What is a voltage regulator?
  maintains a constant dc output voltage, regardless of variations in the input voltage or the load.
Vi
Vo
IL

## Slide 74
Fundamentals of Analogue Circuits
4.3.8 Use of Diode Forward Drop in Voltage Regulation
Q: What characteristic of the diode facilitates voltage regulation?
  A: The approximately constant voltage drop across it (0.7V).

## Slide 75
Fundamentals of Analogue Circuits
Example 4.6:Diode-Based Voltage Regulator
Consider circuit shown in Figure 4.15. A string of three diodes is used to provide a constant voltage of 2.1V.
  Q: What is the change in this regulated voltage caused by
  a ± 10% change in supply voltage
  connection of 1kΩ load resistor
Figure 4.15: Circuit for Example 4.6.

## Slide 76
Fundamentals of Analogue Circuits
With no load, the nominal value of the current in the diode string is given by
Thus each diode will have an incremental resistance of
The three diodes in series will have a total incremental resistance of
I

## Slide 77
Fundamentals of Analogue Circuits
When supply voltage is changed by ±10% (i.e., ±1V), the peak-to-peak change in output voltage will be
r

## Slide 78
Fundamentals of Analogue Circuits
With no load, the nominal value of the current in the diode string is given by
a total incremental resistance of
I
Notes: .

## Slide 79
Fundamentals of Analogue Circuits
When a load resistance of 1kΩ is connected across the diode string, it draws a current of about 2.1mA. Thus the current in the diodes decreases by 2.1mA, resulting in a decrease in voltage across the diode string given by
10V

## Slide 80
Fundamentals of Analogue Circuits
4.4 Operation in the Reverse Breakdown
Region – Zener Diodes
These are referred to as Zener Diodes.
v
I
V
Z0
V
ZK
I
ZK
i
0
Q
V
I
V
Z
Slope
1
r
z

## Slide 81
Fundamentals of Analogue Circuits
Circuit symbol for a zener diode
IZ
VZ
+
-
4.4.1 Specifying and Modeling the Zener Diode

## Slide 82
Fundamentals of Analogue Circuits
v
I
ZT
V
Z0
V
ZK
I
ZK
i
0
Q
V
I
V
Z
Slope
1
r
z
test current
)
(
The diode i–v characteristic with the breakdown region
Δ
Δ
ΔV=ΔI rz
Imax
The Model for the zener diode

## Slide 83
Fundamentals of Analogue Circuits
4.4.1 Specifying and Modeling the Zener Diode
I’ll give you 10 minutes to read pages 203 to 204 of the textbook.

## Slide 84
Fundamentals of Analogue Circuits
The 6.8-V zener diode in the circuit of Fig.4.21(a) is specified to have VZ =6.8V at IZ =5mA, rz=20Ω, and IZK =0.2mA. The supply voltage V+ is nominally 10V but can vary by±1V.
(a) Find VO with no load and with V+ at its nominal value.
(b) Find the change in VO resulting from the ±1-V change in V+. Note that
(∆VO /∆ V+), usually expressed in mV/V, is known as line regulation.

## Slide 85
Fundamentals of Analogue Circuits
(c) Find the change in VO resulting from connecting a load resistance RL that draws a current IL =1mA, and hence find the load regulation (∆VO /∆IL) in mV/mA
(d) Find the change in VO when RL =2kΩ.
(e) Find the value of VO when RL =0.5kΩ.
(f) What is the minimum value of RL for which the diode still operates in the breakdown region?

## Slide 86
Fundamentals of Analogue Circuits
(a) Find VO with no load and with V+ at its nominal value.
VZ =VZ0+rzIZ
→ VZ0= VZ – rzIZ=6.7V

## Slide 87
Fundamentals of Analogue Circuits
(b) Find the change in VO resulting from the ±1V change in V+. Note that (∆VO /∆ V+), usually expressed in mV/V, is known as line regulation.

## Slide 88
Fundamentals of Analogue Circuits
(c) Find the change in VO resulting from connecting a load resistance RL that draws a current IL =1mA, and hence find the load regulation (∆VO /∆IL) in mV/mA

## Slide 89
Fundamentals of Analogue Circuits
(d) Find the change in VO when RL =2kΩ.
(e) Find the value of VO when RL =0.5kΩ.
(e)
(d)
IL=6.8V/2kΩ=3.4mA
IL=6.8V/0.5kΩ=13.6mA

## Slide 90
Fundamentals of Analogue Circuits
(f) What is the minimum value of RL for which the diode still operates in the breakdown region?
IZ =IZK =0.2mA
and VZ ≈VZK ≈ 6.7V
I= (9−6.7)/0.5=4.6mA
IL= 4.6−0.2=4.4mA

## Slide 91
Fundamentals of Analogue Circuits
§4.5 Rectifier Circuits
One important application of diode is the rectifier –
  Electrical device which converts alternating current (AC) to direct current (DC)
One important application of rectifier is dc power supply.

## Slide 92
Fundamentals of Analogue Circuits
step #1: increase / decrease amplitude of AC wave via
power transformer
step #2: convert full-wave AC to half-wave DC (still time-
varying and periodic)
step #3: employ low-pass filter to reduce wave amplitude
step #4: employ voltage regulator to eliminate ripple
step #5: supply dc load

## Slide 93
Fundamentals of Analogue Circuits
4.5.1. The Half-Wave Rectifier
utilizes only alternate half-cycles of the input sinusoid
  Constant voltage drop diode model is employed.
Figure 4.21: (a) Half-wave rectifier

## Slide 94
if vi ≥ VD , the diode turn on, vO =vi−VD.
Fundamentals of Analogue Circuits
Vp−VD

## Slide 95
if vi < VD, the diode turn off. Then vo=0.
Fundamentals of Analogue Circuits
dc-impulse voltage

## Slide 96
Fundamentals of Analogue Circuits
4.5.1. The Half-Wave Rectifier
utilizes only alternate half-cycles of the input sinusoid
  Constant voltage drop diode model is employed.
Figure 4.21: (a) Half-wave rectifier (b) Transfer characteristic of the rectifier circuit (c) Input and output waveforms
PIV = Vs
peak inverse voltage

## Slide 97
Fundamentals of Analogue Circuits
4.5.1. The Half-Wave Rectifier
utilizes only alternate half-cycles of the input sinusoid
  Constant voltage drop diode model is employed.
Figure 4.21: (a) Half-wave rectifier (b) Transfer characteristic of the rectifier circuit (c) Input and output waveforms
vo =vS−VD when vS ≥ VD
vo=0 when vS < VD

## Slide 98
Fundamentals of Analogue Circuits
4.5.1. The Half-Wave Rectifier
Pro’s
  simple
Con’s
  Low efficiency

## Slide 99
Fundamentals of Analogue Circuits
4.5.2. The Full-Wave Rectifier
Q: How does full-wave rectifier differ from half-wave?
  A: It utilizes both halves of the input

## Slide 100
Fundamentals of Analogue Circuits

## Slide 101
Figure 4.22: Full-wave rectifier utilizing a transformer with a center-tapped secondary winding.
Fundamentals of Analogue Circuits
PIV = 2Vs − VD

## Slide 102
Fundamentals of Analogue Circuits
4.5.3 The Bridge Rectifier
An alternative implementation of the full-wave rectifier is bridge rectifier.
Figure 4.23: The bridge rectifier circuit.

## Slide 103
Fundamentals of Analogue Circuits
Figure 4.23: The bridge rectifier circuit.
when instantaneous source voltage is positive,
D1 and D2 conduct while D3 and D4 block

## Slide 104
Fundamentals of Analogue Circuits
Figure 4.23: The bridge rectifier circuit.
when instantaneous source voltage is negative,
D3 and D4 conduct while D1 and D2 block
PIV = Vs − VD

## Slide 105
Fundamentals of Analogue Circuits
4.5.4 The Rectifier with a Filter Capacitor—The Peak Rectifier
A simple way to reduce the variation of the output voltage is to place a capacitor across the load resistor.

## Slide 106
Fundamentals of Analogue Circuits
Figure 4.25 Voltage and current waveforms in the peak rectifier circuit with CR T. The diode is assumed ideal.

## Slide 107
Fundamentals of Analogue Circuits
There are other applications, however, where the signal to be rectified is small (e.g., on the order of 100 mV or so) and thus clearly insufficient to turn on a diode. Also, in instrumentation applications, the need arises for rectifier circuits with very precise and predictable transfer characteristics.
4.5.5 Precision Half-Wave Rectifier—The Superdiode The rectifier circuits studied thus far suffer from having one or two diode

## Slide 108
Fundamentals of Analogue Circuits
For small signal applications, a class of circuits has been developed utilizing op amps together with diodes to provide precision rectification.
Figure 4.27 The “superdiode” precision half-wave rectifier and its almost-ideal transfer characteristic. Note that when vI > 0 and the diode conducts, the op amp supplies the load current, and the source is conveniently buffered, an added advantage. Not shown are the op-amp power supplies.

## Slide 109
Fundamentals of Analogue Circuits
4.6 Limiting and Clamping Circuits
A nonlinear device that limits the output voltage to a particular level.
Be used for waveform transformation, waveform shaping, overvoltage protection……
input
output
limiter

## Slide 110
Fundamentals of Analogue Circuits
If input ≥ Positive limit, output =Positive limit.
If input ≤ Negative limit,
output = Negative limit
otherwise, output =input.

## Slide 111
Fundamentals of Analogue Circuits
4.6 Limiting and Clamping Circuits
Figure 4.31 (d) basic limiting circuits.
vo =v1+VD when vIN ≥ v1+VD
vo=vIN when vIN< v1+VD

## Slide 112
Fundamentals of Analogue Circuits
4.6 Limiting and Clamping Circuits
Figure 4.31 (c) basic limiting circuits.

## Slide 113
Fundamentals of Analogue Circuits
EXERCISE 4.26 Assuming the diodes to be ideal, describe the transfer characteristic of the circuit shown in Fig. E4.26.
vo=vIN when -5V < vIN < 5V

## Slide 114
Fundamentals of Analogue Circuits
EXERCISE 4.26 Assuming the diodes to be ideal, describe the transfer characteristic of the circuit shown in Fig. E4.26.
when vIN ≥ 5V
I

## Slide 115
Fundamentals of Analogue Circuits
EXERCISE 4.26 Assuming the diodes to be ideal, describe the transfer characteristic of the circuit shown in Fig. E4.26.
when vIN ≥ 5V
I

## Slide 116
Fundamentals of Analogue Circuits
4.6.2 The Clamped Capacitor or DC Restorer

## Slide 117
Fundamentals of Analogue Circuits
D
D
4.6.3 The Voltage Doubler
Figure 4.34 Voltage doubler: (a) circuit; (b) waveform of the voltage across D1.

## Slide 118
Fundamentals of Analogue Circuits
The model of the diode is 1N4148,
C1= C2=10μF
Simulation
Observing the output waveform at steady state , we apply the DC supply VK=+5V, VK=0V respectively.

## Slide 119
Fundamentals of Analogue Circuits