## Slide 1: Digital Logic Design and Application Chen Yan Lecture #03
Topic 2-1 Combinational circuits design
——principles

## Slide 2
Principles
Applications
* Logic levels and Gates
Standard Combinational components
Verilog for combinational components
Switching Algebra
logic functions
combinational circuit analysis and design
Topic 2-1 combinational circuits design

## Slide 3: Logic Signals and Gates
Digit logic hide the pitfalls of the analog world by mapping the infinite set of real values for a physical quantity into two subsets corresponding to just two possible numbers of logic ：0 and 1
Infinite set of the real world
Two values in the Digital Logic world
logical abstraction：
  Number system
  Coding
Question1：How?

## Slide 4: Logic abstraction & logic convention
A Y=A’
L H
H L
electrical function table
of invertors
Real world
Logic world
Logic
abstraction
A F
0 1
1 0
positive logic
F=A’
1
0
A G
1 0
0 1
Negative logic
G=A’
1
0
L：0-1.5V
H：3.5-5V
Notes: If it’s not claimed we usually use positive logic conventions in analysis and design afterwards.

## Slide 5
A B F
L L L
L H L
H L L
H H H
Function table
Question 2：Write the truth table for this logic gate in positive and negative logic convention.

## Slide 6: Logic Level
  Physical realization of Logic 1 and 0
    How to get the HIGH and LOW Voltage
VOUT
VIN
Vcc
R
Use transistors as the on-off circuits.
On (1)
L (0)
Off (0)
H (1)
vI
+
–
vO
–
+
iD
+ VDD
RD
D
G
S
If input is L, the transistor is “off” and output is H.
If input is H, the transistor is “on”, output is L.
This on-off Circuit is fact a NMOS invertor (NOT gate).
Basic MOS on-off Circuit

## Slide 7
VCC
Vin
Vout
ON when input is low
ON when input is high
vI
+
–
vO
–
+
iD
+ VDD
RD
D
G
S
Basic CMOS on-off Circuit
CMOS invertor is active pull-up
MOS transistors act like voltage-controlled resistances.
Passive pull-up
NMOS invertor
controllable resistor
ROn：200 Ω
Roff: 1M Ω
Notes: It’s hard to set the value of Rd to ensure both perfect H and L level. While a CMOS transistor which works as controllable resistor can do the job well. we use a P type CMOS transistor to take place of Rd. Then we can get both perfect H and L levels.

## Slide 8: Logic levels
CMOS Logic Levels : Logic 1s and 0s in fact correspond to an acceptable range of voltage change.
Logic 1 (HIGH)
Logic 0 (LOW)
5.0V
3.5V
1.5V
0.0V
LMax
HMin
undefined logic level 
A CMOS Logic Circuit uses not only 5-Volt power-supply voltage, but other power-supply voltages, such as 3.3, 2.7 volts.
30% VDD
30% VDD

## Slide 9: Logic Families
Semiconductor diode
Bipolar junction transistor
Bipolar logic family
Transistor-transistor logic, TTL
Metal-oxide semiconductor field-effect transistor, MOSFET,
Complementary MOS, CMOS

## Slide 10: Logic Families
  A logic family is a collection of different IC chips that have similar input, output, and internal circuit characteristics, but that perform different logic functions.
  Chips of same family can be connected to perform arbitrary logic functions.
  Chips from different families may not be compatible.
  Logic families differ in speed, power consumption and load ability.

## Slide 11: Logic level
A NAND Gate Data Sheets and Specifications 74HC00
Question 3：Find the H and L range?

## Slide 12
Voltage transfer curve of invertors
Vout
Vin
L
H
H
L
UD
DC Noise Margin

## Slide 13
DC Noise Margins
Vout
Vin
L
H
H
UD
L
VOH
VOL
VIH
VIL
4.4
0.1
1.35
3.15
Max
Min

## Slide 14
Vout
VIn
VOH
VOL
VIL
VIH
DC Noise Margin

## Slide 15: DC Noise Margin
HIGH
ABNOMAL
LOW
VOLmax
VILmax
VIHmin
VOHmin
High-state DC noise margin
Low-state DC noise margin
DC noise margin（直流噪声容限） is the voltage amount by which the signal dose not exceed the threshold for a proper logic '0' or '1'.

## Slide 16
DC Noise Margins
High-state DC noise margin：4.4-3.15=1.25 V
Low-state DC noise margin：1.35-0.1=1.25 V
Question 4：Compute the DC noise margins for this circuit.

## Slide 17: Logic Gates
Z = A · B
Z = A + B
Z = A’
AND gate
OR gate
NOT gate

## Slide 18
CMOS Logic Gates
NAND(与非) gate
NOR（或非） gate
Z = (A · B)’
Z = (A + B)’
Question 5：How to get a AND gate ?
Notes: An AND operation can be performed by connect a NAND gate with a NOT gate. An OR operation can be performed by connect a OR gate with a NOT gate.

## Slide 19
Logic Gates

## Slide 20
Logic Gates with non-inverting outputs
CMOS buffer（缓冲器）

## Slide 21
Logic Gates with non-inverting outputs
CMOS AND gate

## Slide 22
An operation (gate) set is COMPLETE（完备） if any logic function can be realized by using logic operations (gates) in the set.
Minimal Complete set(最小完备集): a complete set with no redundant elements.
Examples
{AND, OR, NOT}
{NAND}
{NOR}
Simplest and Lowest Cost
Basic Logic operation / gates
Question 5：Is {AND，OR，NO} a minimal complete set?
Notes: Minimal Complete Set={AND,NOT}, {OR,NOT}

## Slide 23: Fan In （扇入）
CMOS NAND --- more inputs (3)
Inputs can’t be added unlimitedly ---FAN IN
→Use 2n transistors for n-input gate
Z = (A · B · C)’
Z = (X1 · X2·…·Xn)’

## Slide 24: Fan In（扇入）
The maximal number of inputs that a gate have is called fan-in.
The additive “on” resistance of series transistors limits the fan-in of CMOS gates. Typically, Fan-In is 4 for NOR gates and 6 for NAND gates.
Gates with a large number of inputs can be made by cascading gates with fewer inputs.

## Slide 25: Fan out（扇出）
Fan-out of a logic gate output is the maximal number of gate inputs it can connect to without exceeding its worst-case loading specifications.
Fan-out must be examined for both possible output states, HIGH and LOW.
  fan-out = min (HIGH-state, LOW-state fan-out)
  For CMOS load the Fan Out is not a problem
  For Other load the Fan Out must be carefully examined
Notes: For outputting a H level an Ic circuit need to charge the following inputs to H level with providing current, so the parameter is negative in the datasheet;
For outputting a L level an Ic circuit need to discharge the following inputs to L level with absorbing current, so the parameter is positive in the datasheet;

## Slide 26
VCC
Vin
Vout
Explain Board for Fan Out parameter

## Slide 27
LOW state Fan-Out
Example: compute the fan-out for 74HCT driving 74LS
HIGH state Fan-Out
CMOS: 74HCT
IOH = – 4 mA
IOL = 4 mA
IIH = 1 A
IIL = – 1 A
TTL: 74LS
IOH = – 400 A
IOL = 8 mA
IIH = 20 A
IIL = – 0.4 mA
Fan-out
Question 6：Why Fan-out is not 200?
Notes: For 74HCT use the output parameters, for 74LS use the input parameters.

## Slide 28: Reference
“Digital Design: Principles and Practices", 4th Edition, John F. Wakerly, Chap. 3.

## Slide 29
Principles
Applications
*Logic levels and Gates
Standard Combinational components
Verilog for combinational components
Switching Algebra
logic functions
combinational circuit analysis and design
Topic 2-1 combinational circuits design

## Slide 30: Switching Algebra-Axioms
  A1: X = 0, if X  1 X = 1, if X  0
  A2: 0’ = 1 1’ = 0
  A3: 0·0 = 0 1+1 = 1
  A4: 1·1 = 1 0+0 = 0
  A5: 0·1 = 1·0 = 0 1+0 = 0+1 = 1
  Precedence: ( )>NOT > AND > OR
a.k.a. “Boolean algebra”

## Slide 31: Single-Variable Theorems
Identities(自等律): X+0=X X·1=X
Null Elements(0-1律): X+1=1 X·0=0
Involution(还原律): ( X’ )’ = X
Idempotency(同一律): X+X=X X·X=X
Complements(互补律): X+X’=1 X·X’=0
The operations between variable and constant
The operations between variable and itself and it’s complement.

## Slide 32: Two- and Three-Variable Theorems
交换律
结合律
分配律
吸收律
组合律
一致律

## Slide 33: Notices
No logic power law A·A·A  A3
No logic dividing
if A·B=B·C  A=C ??
No logic subtraction
if A+B=A+C  B=C ??
A=1, B=0, C=0
A·B=A·C=0, AC
A=1, B=0, C=1
A+B=A+C, BC
Wrong!
Wrong!

## Slide 34
Covering (吸收律)
X + X·Y = X X·(X+Y) = X
Combining (组合律)
X·Y + X·Y’ = X (X+Y)·(X+Y’) = X
Consensus (添加律/一致性定理)
X·Y + X’·Z + Y·Z = X·Y + X’·Z
(X+Y)·(X’+Z)·(Y+Z) = (X+Y)·(X’+Z)
Some Special Theorems
T9~T11
Notes: All the theorems can be proofed by truth table, Boolean algebra or set theory.

## Slide 35: n-Variable Theorems
DeMorgan’s Theorem （德·摩根定理）
—— Complement Theorem
(A · B)’ = A’ + B’
(A + B)’ = A’ · B’
Xi can be
replaced by
any expression

## Slide 36: Equivalent gates
Notes: Using DeMorgan’s law and equivalent gates digital circuits can be transformed to different structures.

## Slide 37: Circuit Manipulation using DeMorgan’s Law Designing with NAND gates
AND-OR
NAND-NAND
Double inversion cancels

## Slide 38: Circuit Manipulation using DeMorgan’s Law Designing with NOR gates
OR-AND circuit  NOR-NOR circuit
Double inversion cancels

## Slide 39: DeMorgan’s Theorem
Complement of a logic expression:
    , 0  1, Complementing all Variables
  Keep the previous priority
  Notice the ’ out of parentheses
Example1: Write the complement function for each of
the following logic functions.
F1 = A·(B+C)+C·D F2 = (A·B)’+C·D·E’
F1’ = (A’+B’·C’)·(C’+D’)
F2’ = A·B·(C’+D’+E)
F2’ = (A’+B’)’·(C’+D’+E)
Notes: When a logic function F is complicated it’s complement F’ might be simple, and we can implement this logic function by negating the output of F’.

## Slide 40: Duality（对偶）
Duality Rule
    , 0  1
  Keep the previous precedence
FD(X1 , X2 , … , Xn , + ,  , ’ )
= F(X1 , X2 , … , Xn ,  , + , ’ )
T9 and T9’: Covering Law
X + X·Y = X X·(X+Y) = X

## Slide 41: Duality
FD(X1 , X2 , … , Xn , + ,  , ’ ) = F(X1 , X2 , … , Xn ,  , + , ’ )
  0D=1，1D=0； XD=X；
  For function F and G
  （F+G）D= FD·GD； （F ·G）D= FD+ GD
  （F D ）D=F
  If F=G，then FD =GD , vice versa.

## Slide 42
Duality
Dual gates

## Slide 43
Example: Write the Duality function for each of the following Logic functions.
F1 = A+B·(C+D)
F2 = ( A’·(B+C’) + (C+D)’ )’
F1D = A·(B+C·D)
F2D = ( (A’+B·C’) · (C·D)’ )’
Duality
Counterexample:
    X+X·Y = X
    X·X+Y = X
    X+Y = X
X·(X+Y) = X

## Slide 44: Duality and Complement
  Complement:
  [ F(X1 , X2 , … , Xn) ]’ = FD(X1’ , X2’, … , Xn’ )
A B F
0 0 0
0 1 0
1 0 0
1 1 1
positive logic
F = A·B
FＤ = A＋B
F ’= A’＋B’
F’=FD ( A’，B’)
By complementing the variables in the dual function one can get the complement expression of a logic function.

## Slide 45
Eg. Write the duality and complement function for the following logic functions.
F1 = A’·(B+C) + C’·D
F1Ｄ = (A’+(B·C) ) · (C’+D )
F1’= (A+(B’·C’) ) · (C+D’ )
Duality and Complement
Notes: Duality provide us a way of getting the complement function.

## Slide 46: Duality and Applications
A
B
F
C
Once you have the And-Or representation of a circuit it is very easy to get the OR-AND representation of the same circuit.
F=AB+C
A
B
F
C
F =[ FＤ(A ’,B ’,C’ ) ]’
=[ (A’+B’) ·C’ ] ’
And-OR circuit
OR- And circuit
F’
[ F(X1 , X2 , … , Xn) ]’ = FD(X1’ , X2’, … , Xn’ )
F(X1 , X2 , … , Xn) = [FD(X1’ , X2’, … , Xn’ )]’
F’
Notes: Duality provide us a method to implementate the same logic function with different circuit structure.

## Slide 47: Duality and Applications
Replace each gate with it’s dual gate and negates all inputs and outputs.
A
B
F
C
A
B
F
C
And-OR circuit
OR- And circuit
NAND circuit
NOR circuit
F(X1 , X2 , … , Xn) = [FD(X1’ , X2’, … , Xn’ )]’
Question 7：How to keep the precedence in the circuit transformation?

## Slide 48: Reference
“Digital Design: Principles and Practices", 4th Edition, John F. Wakerly, Chap. 4.

## Slide 49
Backups