## Slide 1
Digital Logic Design and Application
Review Yan Bo
School of Information & Communication Engineering, UESTC
Email: yanboyu@uestc.edu.cn

## Slide 2: Grading
Homework: 5%
Lab 20%
Final examination: 75%
Date: ？Jun 2021
Time: ？
Content: 25’ * 4 Questions
Q1 Multiple choice questions
Q2~Q4 Analysis & Design

## Slide 3: Key Points
Analogue system & digital system
Numerical system and Logical Operation
Digital/logic design, including combinational circuits, sequential circuits, and timing analysis
Verilog Hardware Description Language
Electronic Design Automation tools
Von Neumann Computer architecture
CPU architecture, including datapath and controller
CPU design & implement , including specification, partition& verification

## Slide 4: From Boolean Algebra to CPU
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit
1.Notation of number, base conversion
2. Laws of Boolean algebra
Truth table, K-map, logic expression
Design for Combinational circuit
  Gates
  On-shelf chip: Decoder, MUX
  HDL & EDA
Analysis for Combination Circuit
Analogy feature: hazard
STG, State transition/Output table
Design for Sequential Circuit
  F/F＋Combinational circuit
  On-shelf chips: shift register, counter
  HDL & EDA
Analysis for Sequetial Circuit
Analogy feature：
key path，setup time, hold time
Specification： define ISA
Top-design：
  Port
  Datapath＋Controller＋Interconnect
Submodule-design according to ISA
Testbench, performance assessment
1.Basic gates
2.Mninal complete set
3.Analogy feature:noise margin,fan in/out

## Slide 5: From Boolean Algebra to CPU
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit
1.数的表示法，不同进制之间的转换；
2.布尔代数的公理、常用定理；
基本描述方法：真值表，K图，逻辑式
组合电路设计方法
  用门电路实现
  用已有模块搭建：级联，译码器，复用器
  HDL语言描述，综合
组合电路分析方法
电路模拟特性：竞争冒险
基本描述方法：STG, 状态转移/输出表
时序电路设计方法
  用DFF＋组合电路实现
  用已有模块搭建：移位寄存器，计数器
  HDL语言描述，综合
时序电路分析方法
电路模拟特性：关键路径, 建立/保持时间
规格定义： 指令集ISA
顶层设计：
  Port，
  Datapath＋Controller＋Interconnect
子模块设计：根据ISA分别设计
设计验证：testbench设计，性能评估
1.基本门；
2.最小完全集：电路形式的变换；
3.门的模拟特性：噪声容限，扇入，扇出

## Slide 6: Digital system & Analogue system: review the base conversion
(1101.01)2 = ( )10
Binary to Decimal
  Expanded form of polynomial representation
Decimal to Binary
  Radix Divide for integer part
  Radix Multiply for fraction part
    = 1x23 + 1x22 + 0x21 + 1x20 + 0x2-1 + 1x2-2
    = (8)10 + (4)10 + 0 + (1)10 + 0 + (0.25)10
    (13.625)10＝ ( )2
1101
integer
fraction
6
13
3
1
0
2
2
2
2
1
0
1
1
0.625
2
1.250
×
×
×
2
2
0.500
1.000
13.25
Remainder
Integer
.101
Homework chap2
Perform the following expression.
1101 11102 -0011 00102 = (1010 1100) 2 = ( AC ) 16 = ( 254 ) 8 = ( -84 )decimal signed number
Carry/Borrow bit= ( 0 )
Overflow bit= ( 0 )
8421BCD, Gray……?
Notes: Positional Notation--Each bit has a value based on its position
Polynomial Notation (Series Representation)
二进制-十进制
二进制-其它进制

## Slide 7
BCD code
2021-05-11

## Slide 8: From Binary code to Gray code
  XOR
  from right to left
0
1
0
0
1
0
1
1
0
0
0
0
0
1
1
1
1
0
0
0
1
1
1
1
0
1
2
3
4
5
6
7
Gray-code
Decimal
Binary
000
001
010
011
100
101
110
111
Binary: 1 0 0 1 1 1 0 1
1
1
0
0
1
0
1
1
Gray-code:
0
  Reflecting
  from 1-bit to n-bit
7
2021-05-11

## Slide 9: Gates and Logic: other gates
N
N
N
N
XN
X
XN

## Slide 10
Minterm List vs. Maxterm List
Homework chap2
0,2,3,4,6
1,3,4,5,7
0,2,3,4,6
1
1,3
Notes: 1、SOP POS, justΣΠ and j≠I
2、Give F，F’=? JustΣΠ and j=i
3、 Give F，FD=? JustΣΠ and j=[i]n
F1+F2，F1*F2

## Slide 11: Gates and Logic: Duality vs. DeMorgan’s Law
Dual of a logic expression
FD(X1 , X2 , … , Xn ,0,1, + , · )
= F(X1 , X2 , … , Xn ,1,0, · , + )
Complement of a logic expression
F’ (X1 , X2 , … , Xn ,0,1, + , · )
= F(X1 ’ , X2 ’ , … , Xn ’ ,1,0, · , + )
X is not changed !!
X is inverted !!
Chap2.7.2，2.7.3

## Slide 12: Exercise
a
b
c
F(a,b,c)
a
b
FD(a,b,c)
c
F’(a,b,c)
a'
b'
c'
F(a,b,c)
a
b
c
a
b
c
Circle ruler
DeMorgan’s
ruler
a'
b'
c'
F’(a,b,c)
Positive logic
Negative logic
a
b
c
F(a,b,c)
DeMorgan’s
ruler
Change variables
F(a,b,c)
F’(a,b,c)
Homework
Chap2、Chap3
Notes: Duality （对偶定理）

## Slide 13: Digital system & Analogue system: Digital signals versus Analog signals
Noise Margin
Logic 0
Logic 1
Input
Noise Margin
Logic 0
Logic 1
Output
Invalid
Invalid
VIL＝0.8V
VIH ＝2.0V
Vmax＝3.5V
Vmin ＝-0.3V
VOL＝0.35V
VOH ＝2.6V
VCC＝3.3V
VSS＝0V
A particular inverter has:
VILmax = 0.8 V, VIHmin = 2.0 V, VOLmax=0.35V, VOHmin=2.6V.
Then the DC noise margin is (0.6) V in the HIGH state and (0.45)V in the LOW state is.
Notes: threshold
Electronic Aspects of Digital Design
Digital circuits deal with analog voltages and currents and are built with analog components
How to realize Logic 0 and 1 in a Real circuit?
What is the range of analog value with each logic value(0 or 1) ?
How to produce and figure out the signal in a proper range?
The association between Digital and Analog

## Slide 14: Digital system & Analogue system: Digital signals versus Analog signals
Noise margin : A measure of how much noise it takes to corrupt a worst-case output voltage into a value that may not be recognized properly by an input.
Noise margin can ensure that the output signal can be reliably interpret by the following input under different conditions of power-supply voltage, temperature, and output loading
Fan-in : The number of inputs that a gate can have.
As the number of input is increased, designers have to increase the size of series transistors to reduces their resistance and the corresponding switching delay. So, typically, the fan-in of CMOS gates is 4 for NOR gates and 6 for NAND gates.
Fan-out : The number and type of inputs that are connected to a given output.
Too many inputs connected to an output may affect the speed at which the output changes from one state to another, and also destroy the noise margins.
Notes: threshold
Electronic Aspects of Digital Design
Digital circuits deal with analog voltages and currents and are built with analog components
How to realize Logic 0 and 1 in a Real circuit?
What is the range of analog value with each logic value(0 or 1) ?
How to produce and figure out the signal in a proper range?
The association between Digital and Analog

## Slide 15
Input logic
(COMBINATIONAL)
Output logic
(COMBINATIONAL)
Output
STATE-HOLDING
ELEMENTS
Input
States
Output logic
(COMBINATIONAL)
Output
Input
Input logic
(COMBINATIONAL)
Output logic
(COMBINATIONAL)
Output
CLK
Input
States
Mealy FSM
Moore FSM
Digital Logic Circuits: Different Types
CLK
Combinational Logic
Excitation
Excitation
STATE-HOLDING
ELEMENTS
Notes: Moore vs Mealy

## Slide 16
Digital Logic Circuits: Design & Analysis
  Combinational Circuit
  No storage devices
    The output only depends on the current inputs
  The most basic component
    gates: NAND, NOR
  The most commonly used modules
    Decoder/Encoder, MUX/DeMUX, ALU, and so on
    Parity Check circuit, commonly used in communication system
Sequential Circuit
  Combinational circuit + storage devices
    The output depends on the current as well as past inputs(STATE)
      Mealy state machine: the output depends on current input and STATE
      Moore state machine: the output only depends on the STATE
  The most basic component
    Flip/Flop: DFF
  The most commonly used modules
    Register, Counter, and so on
    Serial Signal Detector, Serial Signal Generator
Homework Chap4
Homework
Chap5
Notes: Decoder vs Encoder
Priority Encoder

## Slide 17: Combinational Digital Circuit Design
2.Truth table
A B C F
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
  1.Description: 3-input Majority function, which output is 1 whenever majority of inputs is 1.
1
1
1
1
0
0
0
0
0
C
AB
00 01 11 10
0
1
3.K map
0
0
0
1
1
1
1
4.Logical expression
F = AB + BC + AC
5.Circuit schematic
Notes: K图化简

## Slide 18: Combinational Digital Circuit
CD
AB
00
00
01
11
10
01
11
10
1
d
1
d
1
1
d
1
1
F=CD+ BD +A’BC+ABC’
Notes: 带‘d’的化简

## Slide 19: Logic design with MUX
Lookup Table
F(A,B,C) = m0 + m2 + m6 + m7
8:1
MUX
0
1
2
3
4
5
6
7
S2 S1 S0
S1 S0
4:1
MUX
0
1
2
3
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1
F
1
0
1
0
0
0
1
1
C’
C’
0
1
1
0
1
0
0
0
1
1
A
B
C
F
A
B
C’
C’
0
1
F
2n-1:1 MUX can implement any function of less than n variables
Notes: 151

## Slide 20: Logic design with Decoder and Gates
Z
Y
X
A
B
C
G1
G2A
G2B
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
74x138
F1
+5V
F1 = (X,Y,Z) (0,3,6,7)
While enable input asserted, Yi = mi’=Mi
= M1 · M2 · M4 · M5
= m1’ · m2’ · m4’ · m5’
F2 =  (X,Y,Z) ( 1, 2, 4, 5 )
F2
LSB
MSB

## Slide 21
Combinational Circuits Analysis
  Find a simplified logic for the following circuit :
2.Logical expression
1.Circuit schematic
ABC
A+B+C
AB+BC+AC
F2=AB+BC+AC
F1=ABC+(A+B+C)(AB+BC+AC)’
A | B | C | F1 | F2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
3. Truth table
0
C
AB
00 01 11 10
0
1
4. K map
1
1
1
0
1
0
0
F1
0
C
AB
00 01 11 10
0
1
0
0
0
1
1
1
1
F2
F2=AB+BC+AC
F1=ABC+A’B’C+A’BC’+AB’C’
5.Description: What’s the circuit’s function?
Parity Generator/Checker
（Even Checker）
Majority circuit

## Slide 22: Basic Verilog Modeling
module is a most basic building block of a design.
port_mode port_name1;
port_mode port_name2;
…………
circuit functionality describes an implementation of the corresponding module.
port declarations describes the interface of the component, i.e. input and output ports.
assign statements;
always @(sensitive signals list)
begin
functionality code
end
module module_name (port_name1,_port_name2, …);
port declarations
circuit functionality
endmodule
Interconnect declarations
wire interconnect_name1;
wire interconnect_name1;
…………

## Slide 23: Verilog Design Styles
Components and
interconnects
structural
behavioral
(sequential)
Subset most suitable for synthesis
Testbenches
I1
I2
Y
I1
I2
Y
U1_OUT
module structural (Result, A, B, C);
output Result;
input A, B, C;
wire U1_OUT;
xor U1(U1_OUT,A,B); xor U2(Result,U1_OUT,C);
endmodule
module behavioral (Result, A, B, C);
output reg Result;
input A, B, C;
always @ (A, B, C)
begin
Result = (A XOR B) XOR C;
end
endmodule
dataflow
Concurrent statements
module dataflow (Result, A, B, C);
output Result;
input A, B, C;
assign Result = (A XOR B) XOR C;
endmodule

## Slide 24: Verilog for Combinational Circuit
module Code42( F, I ) ;
endmodule;
always @ ( I )
begin
end
F0
I1
I0
I2
I3
F1
always @ ( I )
begin
if (I[3]) t= 2’b11 ;
else if (I[2]) t = 2’b10 ;
else if (I[1]) t = 2’b01 ;
else t = 2’b00 ;
end
No priority
Priority!
output [ 1:0 ] F;
input [ 3:0 ] I;
assign F = t ；
reg [1:0] t;
case ( I )
1: t = 0 ;
2: t = 1 ;
4: t = 2 ;
8 : t = 3 ;
default: t = 0 ;
endcase

## Slide 25: Verilog for Combinational Circuit

## Slide 26
state
Excitation
EN
MAX
Output logic
Q0
Q1
CLK
State F/F
Input logic
Analysis Steps:
Input logic equations
Output logic equations
State transition equations
State transition/output table
State transition diagram, waveform, etc.
Design Steps:
State transition graph
State transition/output table
State minimization & coding
Chose Storage device (DFF)
Excitation equations
Output equations
Logic circuit diagram
Design & Analysis of Sequential Circuits
step3
step2
step1
Notes: 状态数和DFF的数目
基本步骤：
  确定下一状态函数F 和输出函数G
  将F代入触发器的特征方程得到下一状态Q*
  利用Q*、G构造状态/输出表
  画出状态图、波形图（可选）
  检查电路是否可以自启动
  描述电路功能
State Diagram or State/output table
State minimization
State assignment(coding)
Transition/output table
Chose Storage device (DFF)
Excitation equations
Draw a Logic Diagram
Synchronous
  - we now have a way to store information on an edge (i.e., a flip-flop)
  - we can use these storage elements to build "Synchronous Circuitry"
  - Synchronous means that events occur on the edge of a clock
State Machine
  - a generic name given to sequential circuit design
  - it is sequential because the outputs depend on : 1) the current inputs 2) past inputs
  state machines are the basis for all modern digital electronics
State Memory
  - a set of flip-flops that store the Current State of the machine
  - the Current State is due to all of the input conditions that have existed since the machine started
  - if there are "n" flip-flops, there can be 2n states
  - a state contains everything we need to know about all past events
  - we define two unique states in a machine 1) Current State 2) Next State
Current State
  - the state that the machine is currently in
  - this is found on the outputs of the flip-flops (i.e., Q)
Next State
  - the state that the machine "will go to" upon a clock edge
  - this is found on the inputs of the flip-flops (i.e., D)
  - the Next State depends on - the Current State - any Inputs - we call the Next State Logic "F"
State Transition
  - upon a clock edge, the machine changes from the "Current State" to the "Next State"
  - After the clock edge, we reassign back the names (i.e., Q=Current State, Q*= Next State)

## Slide 27
FSM Analysis
2021-05-11
D1
D0
1). Excitation equations
D0 = Q1+Q0’
2). Output equations
Q = Q1+Q0
3). State transition equations
Q0+ =D0
Q1+ =D1
=Q1+Q0’
=X·Q1’
4). State transition /output table
D1 = X·Q1’
Q1
Q0
S
0 0
0 1
1 0
1 1
X
0 1
10
10
01
00
Q1+Q0+
Q1Q0
00
00
01
00
Q
0
1
1
1
00/0
X=0
01/1
X=1
11/1
10/1
X=1
5). STG
X=0
It is a Moore machine:
if X=1 then the state transits between 01 and 10, the output Q should be 1;
if X=0 then the state reset to 00, the output Q should be 0.

## Slide 28
EN
CLK
1. Excitation equations from input logic
FSM Analysis
Q0
Q1
D0
D1
D0 = Q0·EN’ + Q0’·EN
EN
EN’
Q0
Q0’
Q1
Q1’
2. Output equations
MAX
MAX = Q1·Q0·EN
3. State transition equations
Q0+ =D0
Q1+ =D1
=Q0·EN’ + Q0’·EN
=Q1·EN’ + Q1’·Q0·EN+ Q1·Q0’·EN
4. State transition /output table
S
0 0
0 1
1 0
1 1
EN
0 1
01, 0
10, 0
11, 0
00, 1
Q1+Q0+, MAX
Q1Q0
,0
00
,0
01
10, 0
11, 0
00
EN=0
MAX=0
01
EN=1
MAX=0
EN=1
MAX=1
EN=0
MAX=0
EN=0
MAX=0
EN=0
MAX=0
11
EN=1
MAX=0
10
EN=1
MAX=0
5. State diagram
2-bit Add-up Counter with Enable
6. Timing Diagram
D1 = Q1·EN’ + Q1’·Q0·EN + Q1·Q0’·EN
Notes: Analysis Steps:
Input logic equations
Output logic equations
State transition equations
State transition/output table
State transition diagram, waveform, etc.
Excitation equation (激励方程或驱动方程）
  Express the excitation signals as functions of the current state and input.
  Next state = F (current state, input)
Output equation (输出方程）
  Output = G (current state, input)
Transition equation (转移方程）
  turn a "Characteristic Equation" into an "Excitation Equation"

## Slide 29
FSM Design
Design a Serial Data Detector of 101 (Mealy machine)
Input X=010110100110101110…… Output Z=000100100000101000……
2. State /output table
1. Mealy STG
3. State minimization & coding
4. Excitation equations
6.Logic circuit diagram (DFF)
S0
0/0
S1
S2
1/0
0/0
X/Z
1/0
S3
0/0
1/1
0/0
1/0
S
S0
S1
S2
S3
X
0 1
S1, 0
S1, 0
S3, 1
S1, 0
S+, Z
,0
S0
,0
S2
S0, 0
S2, 0
S
0 0
0 1
1 0
X
0 1
01, 0
01, 0
01, 1
Q2+Q1+, Z
Q2Q1
,0
00
,0
10
00, 0
S
S0
S1
S2
S3
X
0 1
S1, 0
S1, 0
S3, 1
S1, 0
S+, Z
,0
S0
,0
S2
S0, 0
S2, 0
S1
S0
S1
S2
X
Q2Q1
00 01 11 10
0
1
Q2+
Q2+=X’Q1
X
Q2Q1
00 01 11 10
0
1
Q1+
0
5. Output equations
X
Q2Q1
00 01 11 10
0
1
Z
0
0
0
1
0
1
0
0
0
0
1
0
1
0
0
0
1
X
X
X
X
X
X
Q1+=X
Z=Q2X
Q2
Q1
X
Z
CLK
Chap6.4，6.5

## Slide 30: Verilog Design Styles: Sequential circuit/FSM
Components and
interconnects
structural
behavioral
(sequential)
Registers
State machines
Decoders
Subset most suitable for synthesis
Testbenches
dataflow
Concurrent
statements
module behavioral
#( parameter S0=0,S1=1,S2=2 )
(output reg z, input x, clk);
reg [1:0] state, next_state;
always @ ( )
begin
end
always @ ( )
begin
end
endmodule
state <= next_state;
S0
S1
S2
0/0
1/0
0/1
1/0
0/0
x/z
1/1
state
0 0
0 1
1 0
X
0 1
10, 0
10, 0
10, 1
Y1+Y0+, z
Y1Y0
,0
01
,1
01
01, 0
S0
S1
S2
Next state &Output (Combinational )circuit
Update State (Sequential circuit)
negedge clk
state or x
case （state）
S0 : if (x==0) begin --PRESENT STATE/INPUT
next_state=S1; z=0; --NEXT STATE/OUTPUT
end
else begin
next_state=S2; z=0;
end
S1: if (x==0) begin
next_state=S1; z=1; end
else begin
next_state=S2; z=0;
end
S2: if (x==0) begin
next_state=S1; z=0;
end
else begin
next_state=S2; z=1;
end
default: begin
next_state=S0; z=0;
end
end case;
Chap6.4，6.5
Q1: Is it a Moore or Mealy machine?
Q2: What’s the meaning of default branch?

## Slide 31: D-type Flip-Flops with other inputs
Logic Symbol
Function table
  Verilog code
module DFF1 (
);
always@ ( )
begin
end
endmodule
posedge CLK
input CLK, D,
output reg Q
Logic Symbol
Circuit
if ( Clear )
else
or posedge Clear
Q <= 0 ;
Q <= D ;
A D flip-flop with asynchronous Clear
& synchronous Enable
E,
if ( E )
Clear,

## Slide 32: Design circuit by Counter
Please design a modulo-11 counter by 74x163.
1000
0111
0110
0101
0100
0000
0001
0010
0011
1100
1011
1010
1001
1101
1110
1111
QD QC QB QA
1000
0111
0110
0101
0100
0000
0001
0010
0011
1100
1011
1010
1001
1101
1110
1111
QD QC QB QA
1
0
1
0
1
1
1
1
1
1
MSB

## Slide 33
Static hazard in Combinational Circuits
Static 1 hazard
glitch
x2
x3
y2
y1
x1
x1’
z
tpd
tpd
Z = X1+X1’
X3
X1X2
00 01 11 10
0
1
1 1
1 1
This is NOT a Minimal Sum, but it is Hazard Free.
Adjacent means hazard
To remove the hazard

## Slide 34
Timing in Sequential Circuit (DFF)
Propagation delay:
Setup time:
Hold time:
The amount of time from the CLK changed to the output Q changed.
The minimum amount of time AFTER the clock’s active edge by which the data must be stable.
The minimum amount of time BEFORE the CLK’s active edge during which the data must be stable.
tpLH(CQ) , tpHL(CQ)
Data couldn’t
be storage
correctly
tsetup
thold
CLK’s active edge
Data must be stable
Timing violation
Notes: Setup time is defined as the minimum amount of time BEFORE the clock’s active edge by which
the data must bestable for it to be latched correctly. Any violation in this minimumrequired
time causes incorrect data to be captured and is known assetup violation.
Hold time is defined as the minimumamount of time AFTER the clock’s active edge during
which the data mustbe stable. Any violation in this required time causes incorrect data tobe
latched and is known as hold violation.
The setup time in a design determines the maximumfrequency at which the chip can run
without any timing failures.Factors affecting the setup analysis are the clock period Tclk,
Clockto Q propagation delay of the launch flop Tck->q, negative clockskew Tskew, required
setup time of the capture flop Tfs and combinational logic delay Tcomb between the two flops
being timed. Thefollowing condition must be satisfied.

## Slide 35: ISA of our CPU
ISA | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 |  | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | Example
 | Opcode |  |  | *1 | *2 | Rs1/Rd |  | Rs2 |  |  | #imm/offset |  |  |  |  |  |  | 
MOV <Rd>, <Op2> ;Rd  Op2 | 0 | 0 | 0 | 0 | x | Rd |  | Rs2 |  |  | x | x | x | x | x | x | x | MOV R0 , R1
 | 0 | 0 | 0 | 1 | x | Rd |  | x |  | x | #imm |  |  |  |  |  |  | MOV R0 , #0x22
ADD <Rs1/Rd> ,<Op2> ; Rd  Rs1+ Op2 | 0 | 0 | 1 | 0 | 0 | Rs1/Rd |  | Rs2 |  |  | x | x | x | x | x | x | x | ADD R0 , R1
 | 0 | 0 | 1 | 1 | 0 | Rs1/Rd |  | x |  | x | #imm |  |  |  |  |  |  | ADD R0 , #0x22
ADDC <Rs1/Rd> ,<Op2> ; Rd  Rs1+ Op2+C | 0 | 0 | 1 | 0 | 1 | Rs1/Rd |  | Rs2 |  |  | x | x | x | x | x | x | x | ADDC R0 , R1
 | 0 | 0 | 1 | 1 | 1 | Rs1/Rd |  | x |  | x | #imm |  |  |  |  |  |  | ADDC R0 , #0x22
SUB <Rs1/Rd> ,<Op2> ; Rd  Rs1- Op2 | 0 | 1 | 0 | 0 | 0 | Rs1/Rd |  | Rs2 |  |  | x | x | x | x | x | x | x | SUB R0 , R1
 | 0 | 1 | 0 | 1 | 0 | Rs1/Rd |  | x |  | x | #imm |  |  |  |  |  |  | SUB R0 , #0x22
SUBB <Rs1/Rd> ,<Op2> ; Rd  Rs1-Op2-C | 0 | 1 | 0 | 0 | 1 | Rs1/Rd |  | Rs2 |  |  | x | x | x | x | x | x | x | SUBB R0 , R1
 | 0 | 1 | 0 | 1 | 1 | Rs1/Rd |  | x |  | x | #imm |  |  |  |  |  |  | SUBB R0 , #0x22
AND <Rs1/Rd> ,<Rs2> ; Rd  Rs1· Rs2 | 0 | 1 | 1 | 0 | x | Rs1/Rd |  | Rs2 |  |  | x | x | x | x | x | x | x | AND R0 , R1
NOT <Rs1/Rd> ;Rs1 !Rs1 | 1 | 0 | 0 | 0 | x | Rs1/Rd |  | x | x |  | x | x | x | x | x | x | x | NOT R0
JMP <Rs> ;PC  Rs | 1 | 0 | 1 | x | 0 | x | x | Rs |  |  | x | x | x | x | x | x | x | JMP R0
JZ <offset> ;PC  PC+offset (ZF=1) | 1 | 0 | 1 | 0 | 1 | x | x | x |  | x | offset |  |  |  |  |  |  | JZ XXX
JC <offset> ;PC  PC+offset(CF=1) | 1 | 0 | 1 | 1 | 1 | x | x | x |  | x | offset |  |  |  |  |  |  | JC XXX
LDR <Rd>, <Rs> ;Rd  [Rs] | 1 | 1 | 0 | x | x | Rd |  | Rs |  |  | x | x | x | x | x | x | x | LAD R0, R1
STR <Rd>, <Rs> ;[Rd] Rs | 1 | 1 | 1 | x | X | Rd |  | Rs |  |  | x | x | x | x | x | x | x | STR R0, R1
*1: <op2> is in a register (bit12=0 )
or a imm/offset ( bit12=1 )
*2: FLAG register is unused (bit11=0 )
or used (bit11=1)

## Slide 36: ISA of Lab CPU
Opcode supports 16 instructions. So you can add other instructions, like shift,
multiplication.
Rd and Rs can be expressed in 2 bits that means you can operate 4 registers.
Immediate data is expressed in 8 bits.
Opcode | Rd | Rs | Imme | assembly | function
4bit | 2bit | 2bit | 8bit |  | 
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | Mov R1 #02 Mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | Add R1 #08 Add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0100 | 01 | 10 | xxxxxxxx | Sub R1 R2 | R1<=(R1)-(R2)
0101 | 01 | 10 | xxxxxxxx | And R1 R2 | R1<= (R1) bit_and (R2)
0110 | 01 | 10 | xxxxxxxx | Or R1 R2 | R1<=(R1) bit_or (R2)
0111 | xx | xx | 00000001 | Jump #01 | PC<= 1

## Slide 37: TOP-DOWN Design
Control Module
Datapath Module
PART 1
(combination)
PART 2
(combination)
PART 3
(sequential
FSM)
PART 1
(combination)
PART 2
(combination)
PART 4
(Register)
PART 3
(combination)
PART 5
(Counter)
Digital circuit
Top-level module
port-function
Interconnect
PART 4
(sequential
FSM)
Interconnect
Interconnect
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function

## Slide 38: Organization of Center Processor Unit
2021-05-11
37
Data Inputs
Data Outputs
Controller
Datapath
Control Signals
Status Signals
Control Inputs
(Instruction)
Control Outputs

## Slide 39
Datapath depends on ISA
MOV R0 , R1
MOV R0 , #0x22
ADD R0 , R1
ADD R0 , #0x22
ADDC R0 , R1
ADDC R0 , #0x22
SUB R0 , R1
SUB R0 , #0x22
SUBB R0 , R1
SUBB R0 , #0x22
AND R0 , R1
NOT R0
JMP R0
JZ XXX
JC XXX
LAD R0, R1
STR R0, R1

## Slide 40: STG for Control unit

## Slide 41: TestBench Anatomy
TestBench Module
Design Module
Stimulus Generater
Apply Inputs
Response Monitor
Observe Outputs
module My_tb; --TestBench module has no ports
    reg ……….; --Local signals and constants
    wire ……….;
Instantiating module; -- Instantiations of DUT
initial begin ……… end -- Input stimuli: reset
always begin ……… end -- Input stimuli: clock
initial begin ……… end -- Input stimuli: other signals
always @ ( posedge clock ) begin
……… -- Compare results
end
always @ ( posedge clock ) begin
……… -- Display results
end
endmodule
Design Under Test

## Slide 42: A Simple Tester
`timescale 1ns/100ps
module Detector110Tester;
reg aa, clock, rst;
wire ww;
Detector110 UUT (aa, clock, rst, ww);
initial begin
aa = 0; clock = 0; rst = 1;
end
initial repeat (44) #7 clock = ~clock;
initial repeat (15) #23 aa = ~aa;
initial begin
#31 rst = 1;
#23 rst = 0;
end
always @(ww) if (ww == 1)
$display ("A 1 was detected on w at time = %t", $time);
endmodule
No input or output ports
Inputs & Outputs of DUT
The Instantiation of DUT (Detector110 Module)
An initial statement
Generates a periodic signal :
repeats (44) times with (7time steps) delay,
Generates a no-periodic signal
A Verilog System Task: reports the Times at which the ww Variable becomes 1
Time unit

## Slide 43: Design & Implement for CPU

## Slide 44: EDA tools & flow

## Slide 45: PERFORMANCE ASSESSMENT
Consider the execution of a program which results in the execution of 2 million instructions on a 400-MHz processor. The program consists of four major types of instructions. The instruction mix and the CPI for each instruction type are given below based on the result of a program trace experiment. Please give out the average CPI , the corresponding MIPS and the tunning time T when the program is executed on a uniprocessor .
CPI = 0.6 + (2 * 0.18) + (4 * 0.12) + (8 * 0.1) = 2.24
MIPS =(400 * 106) / (2.24 * 106) = 178
T= 2* 106 *2.24/(400 * 106) = 0.012 (s)
Instruction Type | CPI | Instruction Mix
Arithmetic and logic | 1 | 60%
Load/store with cache hit | 2 | 18%
Branch | 4 | 12%
Memory reference with cache miss | 8 | 10%
Notes: 假设一台计算机的时钟频率是100 MHz(每秒百万周期)，具有4种类型的指令，它们的使用率和CPI分别如下表所示。求该计算机的MIPS值以及运行一个具有107条指令的程序所需的CPU时间。