## Slide 1
Chapter 1
Signal & Signal Processing
Why DSP？

## Slide 2
§1 Signals and Signal Processing
Signals—the mathematical representation：
Functions of one or more independent variables.
Signals—generated by natural or technical means .
Signals—carry information.

## Slide 3
1-D signal A speech A Speech Signal
§1 Signals and Signal Processing

## Slide 4
2-D signal An image
§1 Signals and Signal Processing
Disccusion:
Represent a video as a function

## Slide 5
§1 Signals and Signal Processing
Continous-time signal—continuous independent variables .
§1.1 Characterization and Classification of Signals

## Slide 6
§1 Signals and Signal Processing
Discrete-time signal—discrete independent variables.

## Slide 7
§1 Signals and Signal Processing
Analog signals— Continous-time signal
with continuous amplitude.
Digital signals— Discrete-time signal
with discrete-valued amplitudes.
(quantized the values)
(values of real number)

## Slide 8
§1 Signals and Signal Processing
How can we quantize the values of signal?
The real values of amplitudes

## Slide 9
§1 Signals and Signal Processing
by truncation
If the quantization step we chosed is 1,we can get
by rounding
Digits
Digits

## Slide 10
§1 Signals and Signal Processing
The representation of digits in binary form
The Finite Wordlength Effects
by truncation
by rounding
The values of
The values of

## Slide 11
§1 Signals and Signal Processing
If the quantization step we chosed is 0.01,we can get
Digits

## Slide 12
§1 Signals and Signal Processing
A digital signal could be considered that it’s the same as
a discrete-time signal.
The values of
(with the Infinite Wordlength)

## Slide 13
Example. Communication
transmitted
signal
Transmmiter
Receiver
intermediate
input
signal
Received
signal
output
signal
Speech,Text,
Audio,
Video
Voltage, current,
Electromagnetic
Speech,Text,
Audio,
Video
With Information
§1 Signals and Signal Processing

## Slide 14
Example. Get the edge of a picture
§1 Signals and Signal Processing
Edge Map
Original Saturn image

## Slide 15
§1 Signals and Signal Processing
DSP----Processing signals in digital form.
ASP----Processing signals in analog form.
§1.3 Digital Signal Processing
Analog System
Exciting
(Analog signal)
Response
(Analog signal)
It’s generally used for the digital processing of an analog signal

## Slide 16
§1 Signals and Signal Processing
§1.2 Typical Signal Processing and Applications
Signal Processing—to extract useful information
—to change signals for desired purpose.
System
Exciting
(Input signal)
Response
(Output signal)
—normally work as a system.

## Slide 17
analog signals
digital signals(binary)
1.3.1 How to DSP?
§1 Signals and Signal Processing
Figure 1.42 Scheme for the digital processing of an analog signal
Digital Processor :Hardware(VLSI) and Softwares.

## Slide 18
§1 Signals and Signal Processing

## Slide 19
（1）Programmability
Analog system：Modify hardware design.
Digital system：Modify software.
Example：Analog filter, digital filter, adaptive filter
§1 Signals and Signal Processing
1.3.2 Why DSP?

## Slide 20
（2）Precision
Analog system：component specification: resistors have a tolerance 5%; capacitors 20% or worse
Digital system：ADC bits, CPU word width and algorithm
§1 Signals and Signal Processing

## Slide 21
（3）Stability
Analog system：the characteristics of analog system components, resistors, capacitors and operational amplifiers will change along with temperature, humidity
Digital system：will show no variation with temperature throughout their guaranteed operation range.
§1 Signals and Signal Processing

## Slide 22
(4) Anti-noise
§1 Signals and Signal Processing

## Slide 23
Amplify A
Amplify B
Signal generator
computer A
computer B
(5) Repeatability
§1 Signals and Signal Processing

## Slide 24
（6）VLSI (Very Large Scale
Integrated circuit)
§1 Signals and Signal Processing

## Slide 25
(7) Error Correcting Codes
Data retrieval and transmission systems suffer from a number of potential forms of error.
With information in a digital or binary form, we may easily build into the data stream additional “redundant” bits that are used to detect when an error has occurred.
§1 Signals and Signal Processing

## Slide 26
(8) Data Transmission and Storage
The Internet, Compact Disc (CD) and Digital Video Disc (DVD) brought information based on trouble-free high-quality text, audio and video into the office and home.
The fidelity of the digital medium is greater than that of the analog one.
§1 Signals and Signal Processing

## Slide 27: We still need analog processing
（1）Real-Time Processing
Analog system：Besides the delay introduced by the circuit, the processing is in real-time.
Digital system：Decided by the processor speed.
§1 Signals and Signal Processing

## Slide 28: We still need analog processing
（2）Processing very high frequency signals
Analog system：may process microwave, mini-meter-wave, even light wave signals.
Digital system：By the Nyquist Rule，the processing speed is limited by the S/H, A/D and processor speed.
§1 Signals and Signal Processing

## Slide 29: We still need analog processing
(3)The most signals in real would are analog.
If we want to process these analog signals with digital signal processing system, we must change them into digital form first by mixed signal processing.
§1 Signals and Signal Processing

## Slide 30
Electrocardgraph,Seismic,Speech,DVD,
Mobile Phone,ETC.
§1 Signals and Signal Processing
1.3.3 Applications of DSP

## Slide 31: Radar/Sonar
§1 Signals and Signal Processing

## Slide 32: GPS(Global Position System)
§1 Signals and Signal Processing

## Slide 33: Digital Camera
§1 Signals and Signal Processing

## Slide 34: DB Digital AC-3
§1 Signals and Signal Processing