## Slide 1: Electronic System Design 3 Lecture 7.1: Instrumentation Amps and Common Mode Rejection
Dr Duncan Bremner

## Slide 2: …From previous lecture
Problem with previous circuit is that ground is a signal level...
And a sewer for random stray currents
Use PLAN B
Measure the difference between the two leads and let them vary with respect to "Ground” however they like
Common-Mode Rejection

## Slide 3: Common-Mode Rejection (2)
Component X
• Has a big gain (O/P is big, so no more problems)
• Doesn't care what ground potential “???” Is
= Common-mode rejection
• Produces an output voltage with respect to
an explicit third (output ground) input
= Instrumentation Amplifier

## Slide 4: Perfect Instrumentation Amplifier
  • Gain is finite (e.g. 100, 1000..)
  • Gain is pure differential (Function of In(+)–In(–) only)
  • Gain is ideally ZERO for pure common-mode signals
  • "Sense" is feedback connection.
  ‘Ref’ is usually Ground
  If "Sense" connected to "O/P”
  (Where AV is the differential voltage gain and ACM is the common-mode voltage gain)
Only if ‘Perfect’ Inst Amp; Acm = 0

## Slide 5: Instrumentation Amplifier (2)
Application
Instrumentation amp (INA) is connected to thermocouple by
a twisted pair, to avoid magnetic pickup.
Ref is connected to the ground of the O/P connector
  => Voltage between inner & outer of coaxial cable is O/P
R is a large resistor to bleed away bias current (see later)
Circuit is immune to voltage present on "ground"

## Slide 6: Instrumentation Amplifier (3)
Improved:
Since the name of the game is rejecting the average voltage;
symmetry is always a good idea.
Adding a low pass filter (symmetrical) to eliminate radiofrequency interference is a good practical move

## Slide 7: THAT 1510 Microphone Preamp

## Slide 8: Common-Mode Rejection Ratio (CMRR)
Perfect instrumentation amplifier
has a “common-mode” gain =0
In practice no instrumentation amp is perfect: A change in the average (common-mode) voltage will give a change in output
Hambley §9.2

## Slide 9: CMRR(2)
Thus if Av = 100 and ACM = 0.30 (so CMRR = 333 = 50.4dB):
So an input of 333mV on both inputs gives Exactly the same output as 1mV difference between both inputs: With a CMRR of 333 the minimum voltage difference you can detect is 1mV for a common - mode voltage of 300mV.
If the common mode voltage is 1V the minimum detectible differential voltage is 3mV.
Important: minimum detectable signal is assumed when the ‘error’ signal is the same as the ‘real or wanted’ signal.

## Slide 10
Thank you
谢谢