## Slide 1: Electronic System Design 3: The Instrumentation Amplifier Lecture 8.3 More INA Applications
Dr Duncan Bremner

## Slide 2: Application
Classic application: Bridge amplifier (Perhaps a load cell)
Typically, R1=R2, R3=R4(1+D)
*

## Slide 3: Application (2)
Limit on sensitivity is CMRR:

## Slide 4: Application (3)
Magnetic compass
IC includes 2 perpendicular magnetic sensors (one shown)
All 4 resistors approximately equal. All vary.

## Slide 5: Application (4)
Specification: Condition signal with O/P = 1V/Gauss
Total additive error = 0.0175 Gauss (earth ~0.4 Gauss)
= 218µV RTI
Naïve Design (gain = 80):
=12.5mV * 0.0175Gauss

## Slide 6: Application (5)
There are a LOT of error sources in this design!

## Slide 7: Application (6)
Need to simplify, so we can focus on the important sources of error.
1: Gain of input stage is large: All errors due to A3 can be
neglected (they are 40x less important)
2: The bias currents of A1 and A2 are different: The offset
current cannot be larger than the bias current, so we can
ignore it (there is no matching of input currents for
A1 and A2)
3: Reduce the impedance of the feedback network round
A1, A2 so that it is less than the impedance of the bridge,
then only IB(+) will matter, ~ IB

## Slide 8: Application (7)
Errors now due to IB flowing in the bridge, opamp CMRR and
Offset voltage in A1,A2 and resistor CMRR in A3.

## Slide 9: Application (8)
Sources of error: (Total error budget = 218µV)
Budget = 62.5µV
(0.1% resistors: £££)
Gives 218 - 62.5µV = 150µV as total opamp error budget
Opamp VOS(mV) Ib(nA) CMRR(dB) Price
TL071C 10 0.2 70 0.60

## Slide 10: Application (9)
Use total opamp error as
figure of merit;
(resistor CMRR is fixed)
OPA177GP is the lowest cost component that meets the spec!

## Slide 11: Application (10)
Hence complete circuit

## Slide 12
Thank you
谢谢