## Slide 1: Lecture 10: Introduction to Noise In class questions
Dr Duncan Bremner

## Slide 2: Answer the following questions:
1. An amplifier has a vn = 7nV/ rt Hz and an in of 1500fA/rt Hz, what is the optimum source resistance?
2. If an amplifier with a gain of x100 shows an output noise of 1uV/rt Hz, and a source resistance of 12k ohms, what is the noise current of the amplifier?
3. What is the shot noise from a 250uA current source?
4. What is the shot noise from a 1mA current source?
5. What is the signal to noise ratio of a 250uA dc current source?
6. What is the signal to noise ratio of a 1mA dc current source?

## Slide 3: Answer the following questions:
1. An amplifier has a Vn = 7nV/ rt Hz and an In of 1500fA/rt Hz, what is the optimum source resistance? [4.67k ohms]
2. If an amplifier with a gain of x100 shows an output noise of 1uV/rt Hz, and a source resistance of 12kohms, what is the noise current of the amplifier?
[Tricky question; see next slide for answer]
3. What is the shot noise from a 250uA current source? [8.9 x 10-12 A/rt Hz]
4. What is the shot noise from a 1mA current source? [17.8 x 10-12 A/rt Hz]
5. What is the signal to noise ratio of a 250uA dc current source?
[28 x 106 (148.9dB)]
6. What is the signal to noise ratio of a 1mA dc current source?
[56.2 x 106 (155dB)]

## Slide 4: Why is question 2 ‘tricky’
2. If an amplifier with a gain of x100 shows an output noise of 1uV/rt Hz, and a source resistance of 12k ohms, what is the noise current of the amplifier?
If noise at output is 1uV/rt Hz and gain = x 100; then equivalent noise at input is 10nV/rt Hz (vni)
BUT, we have been told that Rsource = 12 k ohms which (by itself) will produce 14nV/rt Hz Thermal noise
Therefore it is IMPOSSIBLE at ~room temperature to achieve 10nV/rt Hz; the circuit would need to be cooled to 151K (-122 degrees C) for a 12 K resistor to achieve this (ignoring amplifier noise).
Question should have read:
If an amplifier with a gain of x100 shows an output noise of 2uV/rt Hz, and a source resistance of 12k ohms, if the amplifier noise voltage is 10nV/rt Hz, what is the noise current of the amplifier? (Assume T = 300K)
We know total noise = 2uV/rt Hz at output which is equivalent to 20nV/rt Hz at input (vni)
Also, if vni 2 = vn 2+ vth 2+ in2 .Rs 2 ; then if vn = 10nV/rt Hz and Rsource = 12 K (14nV/rt Hz)
Then can calculate that vn2+ in 2.Rs 2 = (20nV2 - 14nV2) ; therefore in = 833fA/rt Hz
Optimum Rsource for this system; Ropt = vn / in = 10nV / 833fA = 12 k ohms
This system is optimized for noise