## Slide 1
Wuqiong Luo
Chapter 4 Solution of Electrostatic Problems

## Slide 2: Classification and analysis for solving electromagnetic problems
Static electromagnetic field
Electromagnetic wave
According to the change of time
Chapter
3,4,5,6
Chapter
7, 8,9,10,11

## Slide 3: Classification analysis to solve the problem of static electromagnetic field
Static electric field
According to the types of field
Static magnetic field

## Slide 4
Starting from
Maxwell equations
Conditions
Constitutive relations
boundary conditions
Static electric field problems
Classification according to the charge static or motion
Electrostatic field
Steady current field
Static
Arbitrarily
Uniform motion
Finite

## Slide 5
Contents
4.1 Introduction
4.2 Poisson’s and Laplace’s Equations
4.3 Uniqueness of Electrostatic Solution
4.4 Method of Images
4.5 Boundary-Value Problems in Cartesian Coordinates

## Slide 6
4.1 Introduction
Problems of electrostatic field: electric potential, electric field intensity, and electric charge distribution.
If the charge distribution is given, the electric field intensity and the electric potential can be found by

## Slide 7
In many practical problems the exact charge distribution is unknown (with conducting boundary).
When the conducting bodies have boundaries of a simple geometry, the method of images may be used.
Differential equations must be solved subject to the appropriate boundary conditions. These are boundary-value problems.

## Slide 8: 4.2 Poisson’s and Laplace’s Equation
The two fundamental governing equations for electrostatics are
The electric potential is defined such that

## Slide 9
In a simple medium: linear and isotropic, ε is a constant.
When，
Scalar poisson equation
Laplace equation
Sub-2
Sub-1
Charge
The differential equation of 
Cartesian
Coordinates:

## Slide 10
Ex. The two plates of a parallel-plate capacitor are separated by a distance d and maintained at potentials 0 and V0. Assuming negligible fringing effect at the edges, determine (a) the potential at any point between the plates, (b) the surface charge densities on the plates.

## Slide 11
The potential increases linearly from y=0 to y=d

## Slide 13
13
Solving boundary-value problems ：
Description of boundary value problems
Solution of boundary value problem:
Method of images
Method of Separation of variables
Finite difference method
    ……..

## Slide 14
There may be more than one method for one problem.
Will these methods obtain different solutions?
The uniqueness theorem
A solution of Poisson’s equation (of which Laplace’s equation is a special case) that satisfies the given boundary conditions is a unique solution.
The implication of the uniqueness theorem is that a solution of an electrostatic problem satisfying its boundary conditions is the only possible solution, irrespective of the method by which the solution is obtained.
4.3 Uniqueness of Electrostatic Solutions

## Slide 15
Keep the equations of unknowns unchanged in the solution domain V; at the same time, keep the boundary value of or unchanged on the boundary surface S ; then the solution of the Poisson’s equations or the Laplace’s equations in the solution domain V is unique
The importance of uniqueness theorem
Give the condition of the boundary-value problems with a unique solution.
Provide a theoretical basis for solving the field problems with different methods
Provide a criterion for the correctness of the solution.
The uniqueness theorem
V： solution domain
S：Surface is surrounded by V

## Slide 16
Suppose a volume τ is bounded outside by a surface S0.
Inside the closed surface S0 there are a number of charged conducting bodies with surfaces S1, S2, S3,…., Sn at specified potentials.
Now assume that there are two solutions, V1 and V2 to Poisson’s equation in τ,
Prove

## Slide 17
Also assume that both V1 and V2 satisfy the same boundary conditions on S1, S2, S3,…., Sn and S0. Define a new differential potential:
We see that Vd satisfies Laplace’s equation in τ.
Recalling the vector identity,
and letting f = Vd and A = grad Vd; we have

## Slide 18
where the first term on the right side vanishes. Integration of the Eq. over the volume τ yields
where surface S consists of S0 as well as S1, S2, S3,…., Sn. Over the conducting boundaries, as well as over the large surface S0, Vd = 0. We have
Since the integrand is nonnegative everywhere,
Vd = 0 throughout the volume.

## Slide 19
4.4 method of Images
4.4.1 The basic principle of image method
4.4.2 Point charge and conducting planes
4.4.3 Point charge and conducting sphere
4.4.4 Line charge and conducting cylinder

## Slide 20
1. Introduce the questions
Several examples
A point charge near the grounded conducting plane.
q
q′
No uniformly induced surface charge
Equivalent charge
4.4.1 The basic principle of image method

## Slide 21
A point charge near the grounded conducting sphere.
A line charge near the grounded conducting cylinder, which is similar with the one above, but the equivalent charge is line charge。
q
Non-uniformly induced charge
q′
Equivalent charge
Question: ：Does this equivalent charge exist?
Is this equivalent method reasonable?

## Slide 22
Essence: The effect of the boundary is replaced by one or several equivalent charges, and the original inhomogeneous region with a boundary becomes an infinite homogeneous space.
Key：To determine the number, the positions and the values of the image charges.
Restriction：These image charges may be determined only for some special boundaries and charges with certain distributions.
2. Principle of the method of image

## Slide 23
Purpose: Change the complex boundary-value problem into the problem with infinite single medium space.
Basis：The principle of uniqueness. Therefore, these charges should not change the original boundary conditions. These equivalent charges are at the image positions of the original charges, and are called image charges, and this method is called the method of images.
2. Principle of the method of image

## Slide 24
The number, position and value of the image charge
——"Three key elements"
3. The key points of the application of image method
4. Two principles of determining image charge
Explicit “the effective field” of equivalent solution
Determination of the image charge
The image charge must be located outside the solution domain
The choice of the number, the position and the charge quantity of the image charge is to keep the boundary conditions of the problem unchanged.

## Slide 25
1. The image of the point charge on an infinite grounded plane conductor
It satisfies the original boundary value problem, and the result is correct!
The image charge
The potential functions
When z = 0，
Effective domain
q
q
4.4.2 Point charge and conducting planes

## Slide 26
Solving the induced surface charge density and the total induced charge of the grounded conducting plane
q
The induced surface charge density in the conductor plane is
The total induced charge on the conducting plane is

## Slide 27
2. The image of the line charge on an infinite grounded plane conductor
The images of line charge ：
The potential functions ：
Boundary
Value
When z = 0 ，
Effective
domain
It satisfies the original boundary value problems ,The results are correct！

## Slide 28
3. The image of point charge between the Intersecting semi-infinite grounded conducting plane
q for plane 1:
The image charge is q1=－q，located at(－d1, d2 )
q for plane 2:
The image charge is q2=－q， located at( d1, －d2 )
The solution of the potential function is ：

d1
1
q
d2
2
R
R1
R2
R3
q1
d1
d2
d2
q2
d1
q3
d2
d1
q1 for plane 2 and q2 for plane 1:
The image charge is q3=q， located at( -d1, －d2 )

## Slide 29

q
For the semi-infinite wedge conducting boundary, the method of images is also applicable. However, the images can be found only for conducting wedges with angle given by where n is an integer. In order to keep the wedge boundary at zero-potential, 2n-1 image charges are required.

/3




When an infinite line charge is nearby an infinite conducting plane, the method of images can be applied as well, based on the principle of superposition.

## Slide 30
Ex: The distance between a point charge q and an infinite conducting plane is d ，If moves it to infinity, how much work needs to be done?
Solution：
q'
q
x
 =∞
0
d
-d

## Slide 31
1. The image of the point charge in the grounded conducting sphere
Method: ?
Question：
P
q
a
r
R
d
q
P
a
q'
r
R'
R
d
d'
Boundary conditions！
4.4.3 Point charge and conducting sphere

## Slide 32
Position of the image charge
Charge of the image charge
Constant
q
P
q'
a
R'
R
d
d'
O

## Slide 33
The total induced charge on the surface of the conducting sphere is equal to the image charge of placement.
Find the induced surface charge density and the total induced charge on the conducting sphere
The total induced charge on the conducting sphere is
The induction surface charge density on the sphere is

## Slide 34
Electric Field for a point charge located near a grounded conductor sphere.

## Slide 35
The image charge of a point charge located inside the grounded hollow conducting spherical shell
| q'|>|q|
It has nothing to do with the outer radius b （Why？）
a
q
d
o
b
q'
r
R'
R
a
q
d
O
d'

## Slide 36
The induced surface charge density is ：
The total induced charge on the inner surface of the conducting spherical shell is
Find the induced charge density and the total induced charge on the inner surface of the conductor spherical shell
Is equivalent charge always equal to the total of induced charge ？
NO！

## Slide 37
2 . The image of point charge on the ungrounded conducting sphere
The ungrounded conducting sphere ：
An non-zero equal potential body.
The total induced charge on the spherical surface is zero.
P
q
a
r
R
d
O
Is negative charge distribution the same as the grounded sphere？
Is positive charges uniformly distributed?
q
P
a
q'
r
R'
R
d
d'
q"
O
The surface distribution of the induced charge is ：

## Slide 38
Electric Field for a point charge located near a grounded conductor sphere.
Electric Field for a point charge located near an ungrounded conductor sphere.

## Slide 39
l
P
a
f
d
r
-l
O
An image line charge is put in to represent the charge on the cylinder and placed parallel to it, at a distance d from the axis.
The electric potential with respect to a reference point at a distance r from the line electric charge is
The electric field intensity produced by an infinite line charge of density given by
4.4.4 Line charge and conducting cylinder

## Slide 40
If is also taken as the reference point for the electric potential produced by the image line charge , then and produce an electric potential at a point P on the surface of the cylinder given by
Since the conducting cylinder is an equipotential body, in order to satisfy this boundary condition the ratio must be a constant.
Let , we find

## Slide 41: Using image method to solve the problems
1. Grounded conducting plane
2. Grounded conducting sphere (including the inside and outside of the sphere)
3. Ungrounded conducting spherical (including the inside and outside of the sphere)
Question：
Find the potential function of area with a point charge on the ungrounded infinite conducting plane ？

## Slide 42: Analysis method summary
Methods have been learned and we can solve the problems
1. The problem of infinite single medium space （ 1D,2D,3D problems)
Field—source directly integration method
Integral equation method （Integral form of the Maxwell’s equations ）
Differential equation method (differential form of Maxwell’s equations, Poisson’s equations)
2. Single / non-single medium space problem (1D problems)
Gauss's law and Ampere's Law (the integral equation is simplified to the algebraic equation)
Poisson’s equations (partial differential equation is simplified to ordinary differential equation).
3. Higher dimensional problems in non-single medium space
√ The method of images

## Slide 43
Solving boundary value problems ：
    Description of boundary value problems
    Solution of boundary value problems
Boundary-value problem:
In the given boundary conditions, the solution of the Poisson's equations or Laplasce's equations

## Slide 44
Method of image is useful in solving problems involving free charges near conducting boundaries that are geometrically simple.
Problems consists of a system of conductors maintained at specified potentials and with no isolated free charges, requires the solution of Laplace’s equation.
Problems governed by partial differential equations with prescribed boundary conditions are called boundary-value problems.
4.5 Boundary-Value Problems in Cartesian Coordinates

## Slide 45
Types of boundary value
Given
The first boundary-value problems (or Dirichlet problems)
Given
The third boundary-value problems (or mixed boundary-value problems)
The second-boundary value problems (or Newman problems)
V： solution domain
S：Surface is surrounded by V
Given

## Slide 46
Natural boundary condition（open space）
Requirements：master the mathematical description method to solve complex problems with the idea of boundary-value problems

## Slide 47
Ex：
（ The first boundary value problems ）
（ The third boundary value problems ）
Ex:

## Slide 48
Different specified boundary conditions will require the choice of different potential functions, but the procedure of solving these types of problems is the same-the method of separation of variables;
The solutions of Laplace’s equation are called harmonic functions.

## Slide 49
The dependency relation of the unknown function on several variables (high dimension problem) is changed into Separate dependent relations of each variable (variables can be separated), so that high dimensional problem can be transformed into one dimensional problem.
Method of Separation of variables is a general method to solve boundary-value problems
The theoretical basis of the method of separation of variables is uniqueness theorem
The basic idea of method of separation of variables ：
The basic principle of method of separation of variables

## Slide 50
In rectangular coordinate system, Laplace’s Equation for electric potential is
Let
Substituting it into the above equation, and dividing both sides by X(x)Y(y)Z(z), we have
Where each term involves only one variable. The only way the equation can be satisfied is to have each term equal to a constant.
Let these constants be , and we have

## Slide 51
The three separation constants are not independent of each other, and they satisfy the following equation
The three-dimensional partial differential equation is separated to three ordinary differential equations, and the solutions of the ordinary differential equations are easier to obtain.
or
where A, B, C, D are the constants to be determined.
where kx ，ky ，kz are called the separation constants, and they could be real or imaginary numbers.
The solution of the equation for the variable x can be written as

## Slide 52
or
The solutions of the equations for the variables y and z have the same forms. The product of these solutions gives the solution of the original partial differential equation.
The separation constants could be imaginary numbers. If is an imaginary number, written as , then the equation becomes
The constants in the solutions are also related to the boundary conditions.
It is very important to select the forms of the solutions, which depend on the given boundary conditions.

## Slide 54
In the Cartesian coordinate system， If the potential function has nothing to do with Z ， then the Laplace’s equations is
The  (x, y) is expressed as the product of two one-dimensional functions X( x ) and Y( y ) ，that is
It will be substituted into the Laplace’s equation ，then
Then divided by X( x ) Y( y ) ，next
Separation
constant

## Slide 55
Ifλ＝－k2 ，then
when
When

## Slide 56
If all possible  (x, y) are linearly superimposed., we can get a general solution of the potential functions，that is
If λ＝k2 ,Similarly , we can get that
Separation constant and undetermined coefficients in the general solution is determined by the given boundary conditions.

## Slide 57
Ex: A cover plate is on the infinite rectangular mental conductor slot, which are isolated with each other. The potential of the cover plate is U0, mental conductor slot is grounded. Find the potential distribution in the conductor slot.
Solution：
Since  (0 , y)＝0、  (a , y)＝0，So the general solution is

## Slide 58
Determinate the coefficient

## Slide 59
Expand the U0 using as Fourier series on (0,a)
where

## Slide 60
then
So:

## Slide 61
Ex: Two semi-infinite, grounded conducting planes are parallel to each other with a separation of d. The finite end is closed by a conducting plane held at electric potential  0 , and is isolated from the semi-infinite grounded conducting plane with a small gap. Find the electric potential in the slot constructed by the three conducting planes.
Solution: Select rectangular coordinate system. Since the conducting plane is infinite in the z-direction, the potential in the slot must be independent of z, and this is a two-dimensional problem. The Laplace’s Equation for the electric potential becomes
d
x
y
 = 0
 = 0
 = 0
O

## Slide 62
Using the method of separation of variables, and let
The boundary conditions for the electric potential in the slot can be expressed as
In order to satisfy the boundary conditions and
, the solution of Y(y) should be selected as
From the boundary condition , we have  = 0 at y = 0 , and the constant B = 0. In order to satisfy , the constant ky should be

## Slide 63
We find
Since ，we obtain
The constant kx is an imaginary number, and the solution of X(x) should be
Since    at x = 0 , the constant C = 0, and
Then
Where the constant C = AD .

## Slide 64
Since  =  0 at x = 0 , and we have
The right side of the above equation is variable, since C and n are not fixed. To satisfy the requirement at x = 0, one needs to take the linear combination of the equation as the solution, leading to
In order to satisfy the boundary condition x = 0,  = 0 , and we have

## Slide 65
The right side of the above equation is Fourier series. By using the orthogonality between the terms of a Fourier series, the coefficients Cn can be found as
Finally, we find the electric potential in the slot as
0
d
x
y
 = 0
 = 0
 = 0
Electric field lines
Equipotential surfaces

## Slide 66: Summary
Uniqueness: a solution of an electrostatic problem satisfying its boundary conditions is the only possible solution, irrespective of the method by which the solution is obtained.
Method of Images: when the conducting bodies have boundaries of a simple geometry, the method of images may be used.
Boundary-Value Problems: three types, correctly describe;
Method of separation of variables: transform the high dimensional problem into one dimensional problem

## Slide 67: Homework
4-1, 4-6, 4-7, 4-14, 4-15, 4-21