## Slide 1
Wuqiong Luo
Chapter 7 Time-Varying Fields and Maxwell’s Equations

## Slide 2
Contents
7.1 Faraday’s Law of Electromagnetic Induction
7.2 Maxwell’s Equations
7.3 Electromagnetic Boundary Conditions
7.4 Wave Equations and Their Solutions
7.5 Potential Functions
7.6 Time-Harmonic Fields

## Slide 3
In 1820, Oersted: discovered magnetic effect on current.
In 1831, Faraday: discovered law of electromagnetic induction.
7.1 Faraday’s Law of Electromagnetic Induction
Faraday’s Law of electromagnetic induction
- Reveal the time varying magnetic field generate the electric field;
- It is an experimental law and can be considered as a postulate;
Important conclusions ：
- Under time-varying conditions, Electric field and magnetic field will be induced mutually by each other, forming a unified electromagnetic field .

## Slide 4
Expression of Faraday's law of electromagnetic induction
The electromotive force induced in a stationary closed circuit is equal to the negative rate of increase of the magnetic flux linking the circuit.
The negative sign
- oppose the change--- lenz’s Law

## Slide 5
The changing magnetic field is the source of the electric field.
The induced electric field is a rotational field.
thus：
Understanding of induced electric field ：
As：

## Slide 6
The corresponding differential form is
(1) Magnetic field changes with time while Loop is invariant.
The sources of the electric field have two kinds: Charge, Magnetic field (change with time)
2. Several conditions made magnetic flux change in the loop

## Slide 7
Which is called motional electromotive force , this is the working principle of the generator.
( 2 ) The motion of a conductor loop in a constant magnetic field
( 3 ) The loop moves in a time varying magnetic field

## Slide 8
（1） , Rectangular loop is static ；
x
b
a
o
y
x
Rectangular ring in uniform magnetic field
L
（3） ，and sliding conductor L in rectangular loop moves with velocity .
Solution：(1) Uniform magnetic field do simple harmonic change with time, and loop is static , thus induction electromotive force in the loop is generated by the change of magnetic field, so:
Ex. A uniform magnetic field B vertical through a rectangular ring with a length of a and a width of b , as shown in figure. In the following three cases, solve the induction electromotive force .
（2） , the width b of rectangular loop equals a constant, but the long side increases with time because sliding conductor L moves with velocity ;

## Slide 9
( 3 ) The induced electromotive force in the rectangular circuit is produced by the magnetic field variation and the movement of the sliding conductor L in the magnetic field, so
( 2 ) Uniform magnetic field is constant magnetic field, the sliding conductor on the loop do uniform motion at speed of , thus the induction electromotive force in the loop is generated by the movement of conductor L in the magnetic field, so
or

## Slide 10
Static state ：


Time varying state ：

7.2 Maxwell’s Equations

## Slide 11
1. Total current law
As
Under the condition of time-varying situation, the charge distribution changes with time, according to current continuity equation, we got
Appear contradictory
Not applied in the case of time-varying
Is there other curl source of magnetic field?
Modify to
Conflict resolution

The time varying electric field will give rise to a magnetic field

## Slide 12
Total current law ：
—— Differential Form
—— Integral Form
Total current law reveals that not only the conduction current can induce magnetic field, but also the time-varying electric field can give rise to a magnetic field. It forms an exchange in the nature between the time-varying magnetic field and the time-varying electric field.

## Slide 13
2. Displacement current density
The rate of change over time of electric displacement vector can produce magnetic field, just like current, so it is called "displacement current”.
Attention：
In an insulating medium, there is no conduction current, but there is a displacement current.
In an ideal conductor, there is no displacement current, but there is a conduction current.
In the general medium, there are both the conduction current and the displacement current.
The displacement current only indicates the rate of change of the electric field, which is different from the conduction current, and it has no heat effect.
The introduction of the displacement current is an vital step in the establishment of Maxwell equations. It reveals the important physical concept of the time varying electric field generate magnetic field.

## Slide 14
Differential form
3.Maxwell equations —— Basic equations of electromagnetic field
Integral form

## Slide 15
4. Constitutive relation of medium
Substitute into the Maxwell equations ，we got
Restricted form of Maxwell equation
（ Homogeneous medium ）
The constitutive relation of an isotropic linear medium is

## Slide 16: 7.3 Electromagnetic Boundary Conditions
When letting the height of the flat closed path approach zero, the area bounded by the path approaches zero, causing the surface integrals of and to vanish;
So the boundary conditions for time-varying case are exactly the same as for static electric fields and for static magnetic fields;

## Slide 17
1. The general expressions of boundary conditions
Medium 1
Medium 2
The free surface charge density on the interface
The free surface current density on the interface

## Slide 18
2. The boundary conditions of ideal dielectric interface
that is JS＝0、ρS＝0，so
The tangential component of is continuous

The tangential component of is continuous

The tangential component of is continuous

The tangential component of is continuous

3. The boundary conditions on the surface of the ideal conductor
E2、D2、H2、B2 all equal to zero
The charge density of ideal conductor on the surface is equal to the normal component of

The normal component of on the surface of ideal conductor equals zero

The tangential component of on the surface of ideal conductor equals zero

The current density of ideal conductor on the surface is equal to the tangential component of


## Slide 19: Electromagnetic Field
Starting point
Maxwell’s equations
Conditions
Constitutive relations
Boundary conditions

## Slide 20
Similarly , we can get that
7.4 Wave Equations

## Slide 21
Wave equation of source-free region
Maxwell’s equations Wave equations:
Equations of electric field and magnetic field
Time-varying electric field and magnetic field exist in the form of waves

## Slide 22
Face the problems :
Single medium environment!
Solution of wave equations!
Analysis methods：
Make full use the characteristics of time varying electromagnetic field.

## Slide 23
Questions：
In the electrostatic field analysis ，
how to find its characteristics?
How about in the static magnetic field?
In the time-varying electromagnetic field
analysis, will it play the same role?

## Slide 24
The introduction of potential functions
Calculation of electromagnetic field by means of potential function
Questions：
How to calculation a potential functions ？
Is it beneficial to calculate the electromagnetic field by means of potential functions?
Characteristic
The divergence of the magnetic vector potential can be arbitrary!
7.5 Potential Functions

## Slide 25
Potential function equations
（ D'Alembert Equations ）

## Slide 26
Proof

## Slide 27
Similarly

## Slide 28
Potential function equations
Disadvantages ：
The scalar potential function and the vector potential functions can not be separated!

## Slide 29
Coulomb's gauge ：
Normal conditions of potential functions
Disadvantages ：
The scalar potential function and the vector potential functions can not be separated!

## Slide 30
Lorentz’s gauge ：
Normal conditions of potential functions
Features ：
The electric potential function and the magnetic vector potential function can be separated!
The magnetic vector potential only depends on the current, and the electric potential function only depends on the charge!
The potential functions can be found directly by the Lorentz’s gauge (no need to solve the differential equations)!

## Slide 31
Question：
What is the role of the potential
functions in the time-varying
electromagnetic field ？

## Slide 32
Wave equations of electromagnetic field
Potential functions
Conclusion ：
The two methods is just as simple in the source-free region
The potential equations are much simpler in the source region

## Slide 33
Concept of time-harmonic electromagnetic fields
The physical quantity changes with the time in accordance with the sine law, so it is also called the sine electromagnetic field problem.
7.6 Time-Harmonic Fields

## Slide 34
The favorable factors for solving the problems of time-harmonic electromagnetic fields
Time and space can be Separated to solution！
That is： It can be independent of each other to analyze the physical quantity of spatial variation and temporal variation.
Method：
The time-space relation of physical quantity can be expressed by the complex number
Methods of Real number representation or instantaneous representation
Method of complex representation

## Slide 35
When calculate the time-harmonic quantity about time derivative and integral , the complex representation is more advantageous
Derivative
Integral

## Slide 36
The complex representation of Maxwell’s equations ──Complex vector Maxwell’s equations

## Slide 37
Instantaneous vector
Complex vector
Complex representation of wave equations in the passive region ──Helmholtz’s equations

## Slide 38
Lorentz’s condition
Instantaneous vector
Complex vector
The complex representation of the potential function equations in the active region
Field based on potential functions

## Slide 39
The simple representation of conductive medium──Complex dielectric constant

## Slide 40
Medium loss tangent
For electromagnetic wave, the imaginary part of the complex permittivity of the medium will make the attenuation of the electromagnetic wave。Therefore, in terms of electromagnetic wave propagation，dielectric constant / magnetic permeability with imaginary part of the medium is also called loss medium,
Dielectric
Conductive medium
Magnetic
—— Weakly conducting medium
and good insulator
—— Normal conducting medium
—— Good conductor
Classification of conductive medium
The Ratio of conduction current and displacement current
The ratio of the real and imaginary parts, called loss tangent ：

## Slide 41
Complex representation of wave equation in lossy medium
Lorentz’s condition
Source-free region
source region
Field based on potential functions

## Slide 42
Ex. Find the instantaneous value of the following field in the form of a complex vector
Solution：since
So

## Slide 43
Ex. The Complex vector of electric field intensity is
Solution:
kz and Exm are constant value. Find the instantaneous value of the electric field intensity

## Slide 44
Faraday’s Law of electromagnetic induction
Maxwell’s Equations
Electromagnetic Boundary Conditions
Wave Equations
Time-Harmonic Fields
Summary
Lorentz’s gauge ：

## Slide 45: Homework
7-2, 7-4, 7-7, 7-10, 7-13, 7-25