## Slide 1
Signals and Systems
Lab experiment #3 Introduction
Wang Lingfang (UESTC)
Office Room: KB204
Nov 9, 2021
19:00—22:00

## Slide 2
Lab3
Frequency domain analysis using MATLAB

## Slide 3
References book：
John R.Buck, Michael M. Daniel, Andrew C. Singer. Computer Exploration in Signals and Systems —— Using MATLAB.
lab report template
lab report _template.doc
Required instruments
Computer, MATLAB

## Slide 4: Chief objects for 4 Labs:
Lab1 : Represent signals using MATLAB;
Lab2 : Analysis LTI systems using MATLAB;
Lab3: Frequency-domain analysis using MATLAB;
Lab4: Transform domain analysis using MATLAB.

## Slide 5: Contents
1. Introduction
2. Theoretical background and commands

## Slide 6: 1. Introduction
■ Objective：
Perform the Fourier series using MATLAB
Perform the Fourier transform using MATLAB
Further understand the properties of Fourier transform.
Apply Fourier transform in modulation.
■Related commands:
fft, fftshift, freqz, freqs, filter, residue, Isim
■ Submit your report before: Dec 31, 2021

## Slide 7: 1. Introduction of lab3
■ Exercises ：
Compute the Discrete-time frequency response with freqz.3.2.
Describe the system function by using lsim. 3.3.
Frequency response of a Continuous-time System. 3.9(a)(b).
Properties of the Continuous-Time Fourier Transform. 4.3(a)-(f) .
Perform Partial Fraction Expansion. 4.5(b).

## Slide 8: Contents
1. Introduction of Lab3
2. Theoretical background and commands

## Slide 9: Contents
2. Theoretical background
2.1 fft and fftshift
2.1 fft and fftshift
2.2 freqz and filter
2.3 freqs, residue and lsim

## Slide 10: 2.1 fft and fftshift
■ Discrete-Time Fourier Series
For a signal x[n] with fundamental period N, the DTFS synthesis and analysis equations are given by

## Slide 11: 2.1 fft and fftshift
■ fft
■ Function
Computing the Discrete-Time Fourier Series
■ Command call
y = fft(x);
x : a vector , such as x = [1,3,4,6];
y : the Discrete-Time Fourier Series of x
If x is an N-point vector containing for the single period , then the DTFS of can be computed by a=(l/N)*fft(x), where the N-point vector contains ak for .

## Slide 12: 2.1 fft and fftshift
■ ex1
N=100;
k=(-50:49);
fs=2*pi;
w=fs*k/N;
M=(0:9);
y=ones(1,10);
X=fft(y,N);
Pxx=abs(X)/100;
plot(w,Pxx(1:100));
title('y=fft(x)')
xlabel('x');ylabel('y')
■ Code
■ Figure

## Slide 13: 2.1 fft and fftshift
■ fftshift
■ Function
The function fftshift re-orders the output of fft so that the samples of Y(jω) are ordered in Y from the most negative to most positive frequencies.
■ Command call
y = fftshift(fft(x));
x : a vector , such as x = [1,3,4,6];
y : the Discrete-Time Fourier Series of x, from the most negative to most positive frequencies.

## Slide 14: 2.1 fft and fftshift
■ ex2
N=100;
k=(-N/2:(N/2)-1);
fs=2*pi;
w=fs*k/N;
M=(0:9);
y=ones(1,10);
X=fftshift(fft(y,N));
Pxx=abs(X)/100;
plot(w,Pxx(1:100));
title('y=fftshift(fft(x))')
xlabel('x');ylabel('y')
■ code
■ figure

## Slide 15: Contents
2. Theoretical background
2.1 fft and fftshift
2.2 freqz and filter
2.3 freqs, residue and lsim
2.2 freqz and filter

## Slide 16: 2.2 freqz and filter
■ The frequency response
For an LTI system, if H(ejω) is the frequency response, then

## Slide 17: 2.2 freqz and filter
■ Linear constant-coefficient difference equation
: constant coefficient of x[n];
: constant coefficient of y[n];
x[n]: the input of the system;
y[n]: the output of the system.

## Slide 18: 2.2 freqz and filter
■ freqz
■ Function
Compute the frequency response H(ejω) at N evenly spaced frequencies over for a causal LTI system described by a linear constant-coefficient difference equation.
■ Command call
[H omega] =freqz (b, a, N)
b : constant coefficient of x[n];
a : constant coefficient of y[n];
N: Number of divisions;
H:
omega: (phase）,

## Slide 19: 2.2 freqz and filter
■ freqz
■ Command call
[H omega] =freqz (b, a, N,’whole’)
compute the frequency response H(ejω) at N evenly spaced frequencies over .
b : constant coefficient of x[n];
a : constant coefficient of y[n];
N: Number of divisions;
H:
omega:（phase ）,

## Slide 20: 2.2 freqz and filter
■ ex3
a = [1,0.5,0];
b = [1,0,-0.5];
[H1, ome1]=freqz(b,a,4)
[H2, ome2]=freqz(b,a,4, 'whole')
■ code
■ figure
describe the causal LTI system specified by the system function

## Slide 21: 2.2 freqz and filter
■ filter
■ Function
computes the output of a causal, LTI system for a given input when the system is described by a linear constant-coefficient difference equation.
■ Command call
y=filter(b,a,x)
b : constant coefficient of x[n];
a : constant coefficient of y[n];
x: the input of the system;
y: the output of the system.

## Slide 22: Contents
2. Theoretical background
2.1 fft and fftshift
2.2 freqz and filter
2.3 freqs, residue and lsim
2.3 freqs, residue and lsim

## Slide 23: 2.3 freqs, residue and lsim
■ Linear constant-coefficient differential equations

## Slide 24: 2.3 freqs, residue and lsim
■ Linear constant-coefficient differential equations
■ the frequency response of LTI systems whose input and output satisfy linear constant-coefficient differential equations is easily determined.

## Slide 25: 2.3 freqs, residue and lsim
■ freqs
■ Function
calculates and plots the frequency response of LTI systems whose input and output satisfy linear constant-coefficient differential equations, where the vectors b and a contain the coefficients bk, and ak.
■ Command call
y=freqs(b,a)

## Slide 26: 2.3 freqs, residue and lsim
■ ex4
b = [3];
a = [1,3];
freqs(b,a);
■ code
■ figure
Describe The frequency response of a causal, stable LTI system

## Slide 27: 2.3 freqs, residue and lsim
■ residue
■ Function
calculate the partial fraction expansion of of LTI systems whose input and output satisfy linear constant-coefficient differential equations, where the vectors b and a contain the coefficients bk, and ak.
■ Command call
[r1,p1]=residue(b,a)
a: Constant coefficient of ;
b: Constant coefficient of ;
r1: Contains the numerators of the partial fraction terms;
p1: Contains the roots of the denominators.

## Slide 28: 2.3 freqs, residue and lsim
■ ex5
b = [3];
a = [1,3];
[r1,p1]=residue(b,a)
■ code
■ figure
Disp the partial fraction expansion ofof a causal, stable LTI system

## Slide 29: 2.3 freqs, residue and lsim
■ lsim
■ Function
Simulates the output of continuous-time, causal LTI systems described by linear constant-coefficient differential equations.
■ Command call
y=lsim(b,a,x,t)
a: Constant coefficient of ;
b: Constant coefficient of ;
x: The input of the system;
y: The output of the system;
t: The time samples for the input and output.

## Slide 30
Thanks
2021.11.9